## Slide 1
Meteorology
Forecast maps – NWS surface and NAM upper air; today and the next 3 days
NAM/MOS time series – Denver and Ft. Collins; today and next 3 days;
T, TD, WS, WD, RH, POP, Sky cover
BUFKIT – NAM – time series of cloud amount by altitude, precip, and PBLH
– next 3 days
PBLH from NOAA/ARL WRF-ARW
Wind fields at several sigma levels from NOAA/ARL WRF-ARW
Cloud forecast maps – NAM, GFS, Canadian, GEOS-5
NWS forecaster comments/advice
Fly/no-fly recommendations
DISCOVER-AQ Forecast Briefings

## Slide 2
Air Quality
Air quality yesterday – surface station O3 observations
Air quality forecast maps – NOAA/ARL CMAQ products – O3, NO2, HCHO
today and tomorrow
Ozone forecasts from State agency – today, tomorrow, beyond?
Air quality yesterday – surface station PM2.5 observations
AERONET and MODIS AOD – yesterday
Air quality forecast maps – NOAA/ARL CMAQ product – surface PM2.5
Air quality forecast maps and time series – GEOS-5 aerosol extinction, AOD,
mass concentrations by aerosol type
PM2.5 forecasts from State agency – today, tomorrow, beyond?
DISCOVER-AQ Forecast Briefing

## Slide 3
DISCOVER-AQ Forecast Products
NAQFC - β Forecasting support (NOAA/ARL)
  Initialized at 00 UTC with 60 hours forecast duration
  WRF-ARW (12km N-America & 4 km CONUS)
  CMAQ 4.7.1 (12km CONUS & 4 km DISCOVER-AQ/FRAPPÉ region)
  Includes Aero5 aerosol mechanism (not in NCEP operational version)
GEOS-5 (NASA/GSFC)
  Global at 25 km;
  5-day chemical forecasts twice daily (00 and 12 UTC)
  Total column O3, GOCART aerosols, CO, CO2, SO2 (simple chemistry)
  QFED fire emissions
  Includes aerosol assimilation (MODIS AOD)
  QFED Fire Emissions (NASA/GSFC)
    Near real time estimates based on MODIS Fire Radiative Power (AQUA/TERRA)

## Slide 4
CMAQ4.7.1 | Both CONUS(12 km) & DISCOVER-AQ/FRAPPE (4 km)
Map projection & grid | Lambert Conformal & Arakawa C staggering
Vert. co-ordinate | 42 σ-p unevenly spaced levels
Gas chemistry | Cb05 with 156 reactions
Aerosol chemistry | Aero5 with updated evaporation enthalpy
Anthropogenic emission | 2005NEI as base year, mobile projected using AQS*, area and off-road used CSPR^, point source uses 2012 CEM data
 | WRAP oil and gas emissions data
Biogenic emission | BEIS-3.14
Lateral BC | RAQM (B. Pierce)
AForecast: 12 km nested to 4 km
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0
sigma | 1 | 0.999 | 0.996 | 0.992 | 0.985 | 0.975 | 0.963 | 0.949 | 0.932 | 0.913 | 0.891 | 0.864 | 0.843 | 0.824 | 0.808 | 0.793 | 0.783 | 0.773 | 0.758 | 0.739 | 0.711 | 0.666 | 0.599 | 0.53 | 0.465 | 0.406 | 0.354 | 0.322 | 0.297 | 0.278 | 0.262 | 0.249 | 0.238 | 0.228 | 0.216 | 0.2 | 0.178 | 0.152 | 0.121 | 0.09 | 0.059 | 0.028 | 0
Alt_m | 4.0083 | 20.0568 | 48.2015 | 92.5832 | 161.5484 | 251.4835 | 358.7877 | 488.202 | 640.5597 | 816.8794 | 1031.6737 | 1246.5768 | 1429.2153 | 1591.7849 | 1738.007 | 1857.5046 | 1954.1439 | 2076.278 | 2244.8307 | 2482.669 | 2863.895 | 3479.4963 | 4284.4392 | 5151.2468 | 6033.3231 | 6903.7089 | 7624.7891 | 8150.7998 | 8580.3291 | 8938.4079 | 9247.247 | 9511.8896 | 9750.6913 | 10008.6339 | 10349.3441 | 10836.3458 | 11498.0987 | 12365.8494 | 13440.013 | 14701.7458 | 16245.0793 | 18152.4069 | 22402.6069
42 vertical layers
Air Resources Laboratory/NOAA: DISCOVER-AQ/FRAPPÉ preparation meeting, April 3 2014, Boulder
NAQFC-orecasting support: Initialized at 00 UTC with 60 hours forecast duration
WRF-ARW | Both North America (12 km) & CONUS (4 km)
Map projection & grid | Lambert Conformal & Arakawa C staggering
Vert. co-ordinate | 42 σ-p unevenly spaced levels
advection | RK3 (Skamarock and Weisman (2008))
SW & LW radiation | RRTMG (Iacono et al. 2008))
PBL Physics | Mellor-Yamada-Janjic (MYJ) level 2.5 closure
Surface layer scheme | Monin-Obukhov Similarity with viscous sub-layer
Land Surface Model | NCEP NOAH
Cloud Microphysics | Thompson et al. (2008)
Cloud convective mixing | Betts-Miller-Janjic Mass adjustment
Notes: ^12 km domain is set a bit large to match National AQ Forecasting Capability for side-by-side verification.

## Slide 5
Examples
NOAA Experimental CMAQ
Forecast
3 PM
5 PM

## Slide 6
NASA GEOS-5 aerosol forecast
from: 00 UT 14 Sept.
Cloud cover
Extinction
AOD
GEOS-5 global model at 0.25 deg. resolution;
GOCART aerosols, CO, SO2; includes assimilation of MODIS AOD
Run by Arlindo da Silva at NASA/GSFC
Examples

## Slide 7
GEOS-5 Aerosol Forecast Maps Examples

## Slide 8
Jointly with DISCOVER-AQ
Additional Met & Chemistry Products
Short-term forecasts for aircraft and mobile vans
Decisions on Flight Day and Flight Pattern for C-130
up to 3-5 days out, larger CO regions
Flight Objectives: special events (fires, LRT,..), recirculation, emissions, ...
FRAPPÉ Forecast Briefings
CDPHE/APCD
4 meteorologists will continue to issue statewide and Front Range forecasts for O3 and other pollutants 7 days a week. Includes 9 AM MDT update, a 24-36 hour forecast by 3 PM MDT, and a multi-day outlook. (see presentation by Patrick Reddy)

## Slide 9
FRAPPÉ Forecast Products
Satellite Products
  FINN near-realtime fire emissions (based on MODIS fire counts) (NCAR/ACD)
  MOPITT CO (within 1 day of overpass) (NCAR/ACD)
  IASI CO (~ 4-day delay) (NCAR/ACD)
Met Forecasts
  WRF with assimilation (NCAR-RAL)
    3DVar (no radar DA, 3h UC/12h fcst/1km)
    3DVar (with radar DA, 1h UC/12h fcst) 4DVar (with radar DA, 3h UC/12h fcst)
    RTFDDA (with radar DA, 3h UC/24h fcst)

## Slide 10
Examples
Outside systems:
NSSL (3DVar with radar DA, 1h UC*/12h fcst)
GSD/FAB (LAPS with radar DA, 1h UC/12h fcst)
UK MetOffice (UM-WRF, 6h UC/36h fcst)
NCAR systems:
WRF 3DVar (no radar DA, 3h UC/12h fcst/1km)
WRF 3DVar (with radar DA, 1h UC/12h fcst)
WRF 4DVar (with radar DA, 3h UC/12h fcst)
RTFDDA (with radar DA, 3h UC/24h fcst)
* UC – Update Cycle
Nested WRF domain
1km
1km nowcast/hydro domain
CHILL
S-Pol
3km radar DA domain
NCAR/RAL STEP - Short Term Explicit Prediction

## Slide 11
NCAR/ACD MOPITT and IASI CO
MOPITT CO – available within a day of overpass
IASI CO – about 4-day delay, global coverage 2x/day

## Slide 12
FRAPPÉ Forecast Products
Chemical/Tracer Forecasts
  MOZART-4 global, 5-day forecast (NCAR)
    Full chemistry at 1.9°x2.5° (possibly assimilation of CO)
    Tracer forecasts at 0.5°x0.5° (CO, isoprene-like, ....)
  RAQMS (NOAA/NESDIS)
    Global 1x1 degree on-line chemical and aerosol assimilation and forecasting system
    Assimilation of MODIS AOD, MLS stratospheric O3 profiles and OMI total O3
  WRF-Chem (NOAA/ESRL)
    WRF-Chem on RAPid refresh (RAP) 13km domain; 48 hour forecast
  WRF-Chem Tracers (NCAR/ACD) - added to RTFDDA
  FLEXPART (NCAR/ACD): Forward trajectories for defined sources

## Slide 13
Examples
Cooperative Institute for Meteorological Satellite Studies (CIMSS)
Real-time Air Quality Modeling System (RAQMS)
Global 1x1 degree on-line chemical and aerosol assimilation and forecasting system
Assimilation of MODIS aerosol optical depth, MLS stratospheric ozone profiles and OMI cloud cleared total column ozone
MODIS fire detection and Ecosystem/Severity dependent fire emissions
Real-time verification using US EPA AIRNow surface ozone and PM2.5 measurements

## Slide 14
NCAR MOZART-4 Forecasts
Full chemistry at 1.9°x2.5° http://www.acd.ucar.edu/acresp/forecast/ 5-day forecasts, hourly output, currently operational
Forecasts of tracers at 0.5° horizontal resolution
  Isoprene-like tracer based on MEGAN isoprene emissions
  Anthropogenic NOx tracer from individual cities and/or regions
  Fire CO tracer for various regions
  Others for discussion
  Similar to forecasts for DC3, will be run specifically for FRAPPE
Examples

## Slide 15
NOAA/ESRL RAP-Chem = WRF-Chem on RAPid refresh (RAP) domain
Dx=13km, RAP (met): operational at NCEP with hourly forecast cycle
Experimental RAP-Chem:
  Includes gas-phase chemistry (O3), aerosols (modal approach), Secondary Organic Aerosols ( SOA, Volatility Basis Set approach)
  Chemical boundary conditions from RAQMS or MACC – still to be decided
  NEI 2011 emissions
  48-hr forecasts
  http://ruc.noaa.gov/wrf/WG11_RT/ - different zooms and parameters possible
O3 (ppbV)
Examples

## Slide 16
Examples
NCAR WRF-Chem with Tracers
Added to 3km STEP Forecast:
Inert tracers with specified lifetime
Suggested tracers:
Anthro tracer (NOx like) (area, non-road, point sources)
Mobile tracer (NOx like)
Oil & Gas tracer (ethane like)
Agricultural tracer (emissions needed)

## Slide 17
Examples
NCAR/ACD: Lagrangian particle dispersion products with FLEXPART
trajectories from ground stations / aircraft paths/ sources
forward and backward in time
based on GFS (global) and WRF (regional) model forecasts / analysis
can be convolved with emissions
provides: airmass history and emissions loading, horizontal and vertical information, deterministic trajectory, trajectory clusters, sensitivity maps
24-hr forward trajectory from Denver
on 2013082318 UTC (during SEC4RS)

## Slide 18
8 - 10 AM Review meteorological and air quality products
10 - 11 AM Consult with NWS forecaster and CDPHE air quality forecaster
11 AM – 1 PM Prepare/finalize briefing
1 PM Conduct briefing
Forecast Schedule