## Slide 1: IZAÑA SITE REPORT
Omaira Garcia, Eliezer Sepulveda,
Matthias Schneider, Frank Hase, Thomas Blumenstock

## Slide 2
Since 1999 two Bruker IFS instruments have been installed at the Izaña Observatory (120M in 1999-2005 and 120/5HR in 2005-onwards). Both instruments have been stable, well-characterized (continuous ILS measurements), and consistent with independent observations,…
Izaña FTIR Status
BUT, some instrumental issues last years…
Notes: The idea is to hightlight the good agreement and long-term consistency of the Izaña FTIR measruments with respect to other independent measruements taken at the Izaña observatory (GAW insitu records and NDACC Brewer ozone total columns).

## Slide 3
Izaña FTIR Status
TCCON: March 2018
NDACC: March 2018
Instrumental Issues:
- July 2016-July 2017: Laser
- October 2016-February 2017: Sun tracker
- August 2016-October 2017: Remote LN2
July 2017-September 2017: MIR detectors
…
Data Recording Activities:
There are some gaps in the NDACC and TCCON archives during 2016 and 2017.
Since summer 2017 TCCON data are automatically retrieved by KIT team.
Notes: Explaining the data gaps during the last years.

## Slide 4
On-going Projects
INMENSE (IASI for surveyiNg MethanE and NitrouS oxidE in the troposphere), MINECO, 2017-2019
Analysing the potential of EUMETSAT/IASI for observing global tropospheric CH4 and N2O distributions using the MUSICA/IASI strategy.
MUSICA IASI CH4 at 4.2 km a.s.l.
MUSICA IASI CH4 at 11 km a.s.l.
Long-term mission (2007-2035), Twice daily global coverage; High horizontal resolution (12 km at nadir)
Notes: The idea is to hightlight the IASI’s potential for CH4 and N2O monitoring due to its long-term mission, and temporal-spatial resolution. It provides us useful information especially for CH4 cycle reaserch
The examples of the MUSICA/CH4 time series at different altitudes correspond to surroundings of Tenerife.

## Slide 5
MUSICA IASI at 4.2 km [ppmv]
MUSICA IASI at UTLS [pmv]
NDACC/FTIR at UTLS
Comparisons over long periods
Comparisons of seasonal cycles
GAW in situ
NDACC/FTIR at 4.2 km
INMENSE: Comparisons to different references
Tenerife, 28ºN, 2007-2017
Karlsruhe, 49ºN, 2010-2017
Kiruna, 68ºN, 2007-2017
N2O
N2O
CH4
CH4
AMTD, in review
Notes: Here, an example for Tenerife of the comprehensive validation of MUSICA/IASI CH4 and N2O products by using GAW insitu records and NDACC/FTIR observations. Details on the ATMD paper under review.
The left panels show the scatter plots of the whole time series distinguishing the measurement year for GAW and FTIR at lower troposphere (4.2 km asl) and for FTIR at UTLS (12 km asl).
Comments: The overall precision is about 2% for N2O and CH4, with a bias within 2%.
The right panels display the comparison of the seasonal cycles relative to the long-term background (after temporal decomposing the observed time series). Comments: N2O: sensitivity limited to the upper troposphere, CH4: sensitivity in the upper troposphere, profiling capability at low latitudes (additional sensitivity in the free troposphere
5

## Slide 6
¿Why Madrid?
Highest populated city of Spain (3.2 million population, 7% of total population of Spain)
Very concentrated city (mainly diffuse CO2 and CH4 sources)
Commitment to GHGs emissions control
Field Campaign in Madrid in 2018
 6 Bruker EM27/SUNs: 1 (AEMET) + 3 (KIT) + 1 (UH) + 1 (TUM)
MEGEI-MAD (Monitoring Greenhouse Gas Concentrations in the city of Madrid, Spain), AEMET, 2018.
On-going Projects
2 weeks in September/October
XCO2 and XCH4 (emission fluxes?)
Our EM27/SUN is already installed at Izaña.
Notes: Just to hightlight that our EM27/SUN spectrometer is already installed at the observatory and we have planned a field campaign in Madrid in september/october 2018 with the collaboration of the KIT (Frank Hase and Thomas Blumenstock), University of Heidelberg (Andre Butz) and Technical Unviersity of Munich (Jia Chen).

## Slide 7
VALIASI (VALidation of IASI level 2 trace gas products), EUMETSAT Fellowship, 2016-2018.
Evaluation of the quality and long-term consistency of operational EUMETSAT/IASI trace gas products
Arrival Heights
Lauder
Wollongong
Reunion Island
Izaña
Junfraujoch
Kiruna
Ny-Alesund
An example for Ozone Total Column Comparison: Bias (IASI-NDACC/FTIR) of the TOC amounts with the associated scatter (IP68) for IASI/O3 datasets (FORLI left panels and EUMETSAT right panels) for all surface types and periods (V5: September 2010-September 2014; V6: September 2014-December 2016). The bottom panel shows the Degree of Freedom (NDACC/FTIR in stars and IASI in circles).
On-going Projects
Notes: 7
Here, an example of the comparison studies performed within EUMETSAT fellowship VALIASI for the validation of IASI trace gas products. Two IASI algorithms are compared (FORLI from LATMOS and EUMETSAT operational).
7

## Slide 8
1. Yela, M., et al: Hemispheric asymmetry in stratospheric NO2 trends, ACP, 2017.
2. Bader, W ., et al:, The recent increase atmospheric methane from 10 years of ground-based NDACC FTIR observations since 2005, ACP, 2017.
3.Barthlott, S., et al: Tropospheric water vapour isotopologue data (H216O, H218O, and HD16O) as obtained from NDACC/FTIR solar absorption spectra, ESCD, 2017.
4. García, O. E., et al: Upper tropospheric CH4 and N2O retrievals from MetOp/IASI within the project USICA , AMTD, in review, 2017.
5. Schneider, M., et al: MUSICA MetOp/IASI {H2O,δD} pair retrieval simulations for validating tropospheric moisture pathways in atmospheric models, AMT, 2017.
6. Steinbrecht, W., et al: An update on ozone profile trends for the period 2000 to 2016, ACP, 2017.
7. Borger, C., et al., : Evaluation of MUSICA MetOp/IASI tropospheric water vapour profiles by theoretical error assessments and comparisons to GRUAN Vaisala RS92 measurements, AMTD, in review, 2017.
8. Wunch, D., et al: Comparison of the Orbiting Carbon Observatory-2 (OCO.2) XCO2 measurements with TCCON, AMT, 2017.
9. Cuevas, E., et al.,: Izaña Atmospheric Research Center Activity Report 2015-2016, WMO/GAW Report No. 236, 2017.
10. Borsdorff, T., et al.,: Mapping carbon monoxide pollution from space down to city scales with daily global coverage, AMTD, in review, 2018.
11. Gaudel, A, et al.,: The Tropospheric Ozone Assessment Report: Present-day distribution and trends of tropospheric ozone relevant to climate and global atmospheric chemistry model evaluation, Elem Sci Anth, 2018.
12. Vigouroux, C., et al.,: NDACC harmonized formaldehyde time-series from 21 FTIR stations covering a wide range of column abundances, AMTD, in review, 2018.
Publications related with Izaña FTIR activities: 2017-2018
2017
2018