## Slide 1: MIR Site Report: Wollongong, NSW
Nicholas Jones, David Griffith, Clare Murphy, Nicholas Deutscher, Voltaire Velazco, Graham Kettlewell, Beata Bukosa

## Slide 2: Site Report: Wollongong, NSW
Administrative matters
  The MIR programme is funded through Australian Federal grant till end of 2020)
  NJ is funded at 50%.
Added formal errors per spectrum (using idl code by Dan Smale which in turn is based on an older NCAR version) plus other sundry changes (surface temperature) for inclusion in the HDF file.
Archiving: updated HDF O3 (to Sep 2017). HNO3/HF ready, while N2O/HCl/C2H6 nearly ready to go (into the archive) and will also replace previous versions.
Sfit4 operational code with a single output file?. Testing sfit4_0.9.7.0 but issues with compiling.
Instrument performing well, no current significant issues but lost 6 months of data (Sep 2017 – March 2018 due to problems with solar tracker)
Data: 12 months April 2017-March 2018, 104 measurement days for MIR (180 in 2016-2017).
Worked on procedures for rapid delivery of CO, CH4, and HCHO for SP5 (almost there)

## Slide 3
HITRAN 2018
HITRAN 2018 - modified
HITRAN 2008

## Slide 4
Haloe Total column, computed from v19 data (includes pressure/Temp/Z grid) within 500km
ACE total column computed from v3p6 data selected using online selection tool within 500km on given pressure/Temp grid
Used 2004.5-2006 period mean to scale all Haloe data upwards by a factor of 1.17

## Slide 5
HF trends 1996-2016
Kasima (Thomas Reddmann, KIT, “first try”)
Model run with a horizontal resolution of ~5.6° and vertical resolution of about 1 km in the stratosphere (varying).
Model was nudged to ERA-Interim data.
The run was started in 19980101. Model data have been interpolated to longitude 150.88 and latitude -34.41.