## Slide 1: Mobile Optical Remote Sensing Measurements to Quantify Diffuse Emissions Johan Mellqvist, Chalmers University of Technology Sweden

## Slide 2: Fixed column measurement of CO, NH3, HCHO using solar FTIR in Mexico City during MCMA 2003 experiment
de Foy,., J., Mellqvist, J.,. Grutter, M., ..A. & Molina, L. (2007) ACP. DOI: 10.5194/acp-7-781-2007.
Bruker OPAG 22 (0.5 cm-)
with MCT; NPL solar tracker
SFIT 2 evluation

## Slide 3: Geographical variation of the CO column from Cenica to Pachuca Hildalgo, April 13 2003, fixed measurements
DCO=1.5e18 molecules/cm2

## Slide 4
Temporal variation of the CO column at central Mexico city (Merced), on April 28 2003. Fixed measurements

## Slide 5: Column Measurements CO and NH3 south of Mexico City in Santa Anna 28/4 2003. Wind turned.
DNH3~2e15
DCO~1e16
DNH3/DCO=2.2 %

## Slide 6
Atmospheric columns for key species is estimated from spectroscopic analysis of direct solar IR light and zenith scattered UV light.
The flux is obtained by intgrating the columns across the plume and multiplying with the wind . The typical uncertainty is 20-30%
Doppler LIDAR
Flux
Unspeciated alkanes C2-C10, alkenes, alcohols CO, NH3, HCl....
Solar Occultation Flux
SOF
Notes: sattelites

## Slide 7: Typical SOF hardware
IR cube (0.5 cm-) with InSb/MCT
detector (700- 7000 cm-1) and
custom made fast responding
solar-tracker
Wind LIDAR for wind profile
measurements

## Slide 8: Realtime and post analysis software
Realtime program showing a 2 D map
of the measurement. The spectral fit and
the retrieved column and the gasflux is
obtained
Database in which column measurements, position and wind is merged. Area emissions for defined areas are obtained.

## Slide 9
For alkanes the CH stretch region at 3 µm is being used.
A few calibration species (C2, C3 C8) are fitted for the total alkane column.
The retrieval error in mass is typically 5%.
Our own retrieval code with cross sections from PNL/Hanst and HITRAN. For strong absorbers MALT or SFIT
SOF-measurement of alkanes from a ship in the Göteborg harbor.

## Slide 10: Example of Ammonia column measurement from chemical plant Scientific campaign Tianjin/Beijing 2016
Ammonia 551 ± 46 kg/h

## Slide 11: Methodology on how to measure area emission SOF VOC measurements on a refinery tank farm in Sweden (the color scale correspond to alkane value)
”
Area emission = Outflow – Inflow
Wind
风
VOC
(alkane)

## Slide 12: Standardisation/ Validation
The SOF technique is Best Available Technology (BAT) in Europe for refinery measurements. From 2019 refineries are forced to validate their emission estimates by measurements.
The SOF technique is being standarized in European CEN TC 264/WG 38. A protocol has been finalized.
  Validation experiments at abandoned refinery in France and demonstration measurements at a refinery in Netherlands.
Many other studies, show about 30 % uncertainty. Single sources more diicult than more complex ones.
Notes: Point out blind strudies

## Slide 13: Controlled source releases of propane inside an abandoned process unit as part of CEN validation work.
Releases from 4 nodes by external reviewer and measurements 50-500 m
downwind.
Notes: Blind stduy with referee

## Slide 14: SOF is a statistical method requiring averaging of several transects to minimiooze wind variability .
A bootstrap analysis was performed on 7 repeatability tests (67 measurements) in the controlled source release.
Figure shows how the statistical distribution of the random error varies with the sample size N.
In the SOF protocol 4 measurements is required, corresponding to 1s =25%

## Slide 15: SCAQMD study (Los Angeles): VOC emissions from 6 refineries and 61 small sources in 7 source categories in fall of 2015 and NH3 from cattle in Chino (Reports: http://www.aqmd.gov/fenceline-monitoring)

## Slide 16: Oil and gas production, Signal Hill
SOF measurements of alkanes. Blue areas correspond to oil wells, cisterns and Derricks and purple areas to treatment plants and tankfarms
Oil wells,
Gas treatment ,
Gas treatment ,
Oil wells,
Oil wells,

## Slide 17: Overall measured VOC results
Source Category | No. of Units meas. | Unit Type | Total Alkane [kg/h] | BTEX | Benzene | CH4
Oil & Gas Wells | 106 | Derricks + small tanks | 138 | 7 % | 1.2% | 53%
Tank Farms, Terminals & Depots | 343 | Storage tanks | 317 | 8 % | 1 | 85%
Petroleum Treatment Sites & Small Refineries | 8 | Sites | 498 | 6 % | 1% | 47%
Offshore - Platforms, Fuel Islands & Fuel Barges | 7 | Sites | 69 | n.m. | n.m. | n.m.
Other Significant VOC Sources | 7 | Various | 286 | n.m. | n.m. | 41%
Gas Stations | 8 | Sites | 10 | 24 % | 3% | 25%
Flux, All measured small sources |  |  | 1318 | 68 | 12 | 648
Big Refineries ( | 6 | Sites | 1130 | 113 | 11 | 700

## Slide 18
VOC emission sources in LA basin measured by optical flux measurements and scaled-up emission 2015
Total VOC emission
(Alkanes and BTEX)
Measured: 3128kg/h
Scaled-up : 13317 kg/h
(based # sources)

## Slide 19: SOF study indicates that the VOC emissions from the oil and gas sector are 8.6 higher than reported in CARB inventory value, i.e 13317 instead of 1550 kg/h. This would increase the emissions of VOCs from all sources in the LA basin by more than 70%, including area, mobile and stationary sources .
SOF with extrapolation to all sources
Merge of optical measurements
and emission inventory by CARB 2012
New VOC emission budget LA basin

## Slide 20: Alkane emissions from industrial complexes
Source region | SOF (kg/h)* | Inventory (kg/h) | % capacity | Factor
Göteborg 2005-2017 3 refineries | 1100 | 1100 | 0.05% | 1
Antwerp 2010, 3 refin.+chem | 5510 | 715 | 0.07%*** | 7.7
Le Havre 2008**** 2 refin. | 4407 | 1048 | 0.04%*** | 4.2
Rotterdam 2008***** 6 refineries | 5553 | 1265 | 0.045%*** | 4.4
CA, Bay Area 2013 3 refineries | 877 | 192 | 0.04% | 4.6
CA, LA basin 2013/2016 6 Refineries Oil production | 1242 8076* | 194 38 | 0.02% | 6 211
Houston ship channel 2006/2009/ 2011/2012 multiple refin. + chem | 11600 | 850 | 0.14%*** | 14
China 2 Tianjin Refineries 2016 1 Fushun refin. 2014 Fushun Oil sand refin. 2014 | 2000 1278 1290 | 3500** 1560** | 0.1% 0.14% 5.6% | 0.6 0.8
*interpolated from 1800 kg/h, causes 70 % increase in the total projected VOC emissions for the SCAB ** Tianjin Academy of Environmental Planning: 0.18% of capacity *** 0.01% assumed for inventory **** Revisited 2016

## Slide 21
Validation measurements show uncertainties of 20-40%.
Large discrepancy in LA of predicted VOC emissions from stationary and small sources compared to CARB inventory (factor 8). Will cause significant change in total VOC emissions in LA.
Similar differences observed in many parts of the world (Europe, China, Middle east).
On going projects
  Standardisation CEN and OTM
  California (CARB)- diffuse emissions and health impact. Field campaign CA (oil&gas, dairies, landfills, refineries) . Plan include two EM 27 sun from COCOON.
  China (campaign 2019 Beijing)
  Building mobile lab for SCAQMD and Chinese institute
Conclusion and outlook

## Slide 22: References
Mellqvist, J., J. Samuelsson, J. K. E. Johansson, C. Rivera, B. Lefer, S. Alvarez, and J. Jolly (2010b), JGR: Atmospheres, 115(D7), doi:10.1029/2008JD011682.
Johansson, J., Mellqvist, J., et al., 2013a, JGR– Atmospheres, 2013JD020159R.
Johansson, J. K. E., J. Mellqvist, J. Samuelsson, B. Offerle, B. Lefer, B. Rappenglück, J. Flynn, and G. Yarwood (2014), JGR, 118, doi:10.1002/2013JD020485.
Johansson, J. K. E. (2016), Doctoral thesis, 162 pp, ISBN 978-81-7597-316-6, Chalmers University of Technology, Gothenburg.
Johansson, M., C. et al, 2009, Atmos. Chem. Phys., 9, 5647–5653
Rivera, C. et al., (2010), JGR, 115, D08301, doi:10.1029/2009JD012675
Rivera , C.,), Dissertation, ISBN 978-91-7385-317-0, ISSN 0346
Rivera, C., J.A. Garcia, B. Galle, L. Alonso, Y. Zhang, M. Johansson,Matabuena, and G. Gangoiti (2009b), J. Remote Sens., vol 30, no 12, p3191–3204