## Slide 1
Johan Mellqvist, Glenn Persson
Space, Earth and Environment
Chalmers University of technology
Göteborg, Sweden
johan.mellqvist@chalmers.se
Site report - Harestua – 23 years
60.2°N, 10.8°E, 596 m.a.s.l.

## Slide 2
Dobson SMHI
O3
µ-wave Chalmers
O3, CO. mesosph
FTIR Chalmers reservoir species
UV/VIS Bira
O3, NO2, BrO..
Denmark
Norway
Sweden
ODIN (µ-wave and UV)
O3, H2O, ClO, NO2, N2O >20 km

## Slide 3: Comparison FTIR Harestua and Dobson in Norrköping

## Slide 4: HCl and ClONO2 summer, 5 years averages
HCl
ClONO2
Total Cl

## Slide 5: HCl summer versus full year , 5 years averages
Summer
Full year

## Slide 6: Ethane and CO columns at Harestua. Ethane used to have the same trend as CO but is now increasing (fracking?).

## Slide 7
Bruker 125 M, remotely controlled through internet
Instrument installed in May 1994 and upgraded in Aug. 2008 to 125 M (Brault aquisition )
Home made solar tracker since 2006, before solar coelistat of solar observatory.
Remote LN2 filling and meteorogical parameters (p, T and RH), 2008
  New beamsplitter and laser and new aperture plate, Nov. 2009
  HBr cell #13, new since Aug 2016

## Slide 8: Line shape measurements of HBr cells, # 13 and new one since Aug 2016. But it started leaking end 2017, so now we use old one. .
New HBr cell

## Slide 9: Measurements at Harestua
1120 measurement days since Nov 1994
44 measurement days in 2017 (normally +50). Scanner and solar tracker problems plus weather.
HBR cell measurements shows in general good quality
Data in AMES format reported to the NDACC archive up to the end of December 2015, available as aems until 2016. HDF 4 Geoms not yet available since some of the erroranalysis is missing (see next slide).
  Species reported are C2H6, CCl2F2, CH4, ClONO2, CO, COF2, HCFC22, HCl, HF, HNO3, N2O, NO2 and O3.
Funding from Swedish EPA on an annual basis, (semi secure).

## Slide 10
SFIT2 v3.94 algoritm, (CH4, CO, HCL, HCN, HNO3, N2O,O3). SFIT2 v3.81, other NDACC species
Hitran 2004/Hitran 2008 linelist
Apriori EMEP profiles
NCEP data for pressure and temperature profiles
ILS using HBr cell and Linefit, ver. 9
Spectroscopic retrieval details

## Slide 11: Future
  Funding secured for running site with 0.5 Engineer, data in Swedish EPA database.
  This summer switching to SFIT4 with full error characterization and WAAC apriori profiles
  HD4 Geoms reporting during the fall
  Need to get new instrument within the next couple of years
  We would like to start a new measurements site in Northern India, Swedish-Indian research platform available, I am in the board
  Science
    Joint ethane paper, Mahieu in progress
    Can we have a joint paper on CFC 11/CFC 12
    Field campaign with SOF in central valley, CA. Hope to include two EM 27 sun from COCOON.