## Slide 1: Rikubetsu site report –NDACC measurements
Tomoo NAGAHAMA
Institute for Space-Earth Environmental Research (ISEE)
Nagoya University (NU), Japan
and
Isamu MORINO
National Institute for Environmental Studies (NIES)
Japan
NDACC-IRWG/TCCON meeting in Mexico, June 11 – 14, 2018

## Slide 2
Rikubetsu (43.5N, 143.8E, 380 m)
NIES Bruker 120/5HR FTIR
Recent status of the instrument is
presented at a poster (Morino et al.)
HERE

## Slide 3: Measurements, analysis and archives
> NDACC measurements are carried out typically 1-2 per month.
(32 days in the last 12 months)
> Retrievals of the vertical distribution of 12 species
(10 NDACC-standard + OCS, CCl4) from all the spectra taken with
STEL and NIES FTIRs (1995.5 - 2018.4) by using SFIT4 (Ver. 0.944)
have been made.
> All the retrieved data for the NDACC standard species until April
2018 are archived at the NDACC DHF (version 002 dataset).
Chart: 
| 41640 | 41671 | 41699 | 41730 | 41760 | 41791 | 41821 | 41852 | 41883 | 41913 | 41944 | 41974 | 42005 | 42036 | 42064 | 42095 | 42125 | 42156 | 42186 | 42217 | 42248 | 42278 | 42309 | 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826 | 42856 | 42887 | 42917 | 42948 | 42979 | 43009 | 43040 | 43070 | 43101 | 43132 | 43160 | 43191
 | 4 | 3 | 2 | 3 | 2 | 3 | 2 | 2 | 1 | 4 | 3 | 3 | 5 | 5 | 3 | 4 | 5 | 1 | 5 | 1 | 2 | 5 | 2 | 4 | 1 | 0 | 1 | 3 | 3 | 1 | 3 | 1 | 1 | 4 | 4 | 1 | 0 | 1 | 2 | 2 | 1 | 2 | 1 | 1 | 2 | 1 | 1 | 2 | 3 | 8 | 4 | 4
Table: Number of NDACC measurement days with Rikubetsu NIES FTIR
32 days
42 days
23 days
19 days
2014
2015
2016
2017
16 days
2018

## Slide 4
O3
HCl
HF
HNO3
ClONO2
CH4
HCN
CO
N2O
C2H6
Time series of total columns over Rikubetsu

## Slide 5: Data usage & activities
・Presentations
JpGU-AGU2017: overall (Nagahama et al. ), CO (Sunada et al.)
JSAC2017: HCN (Nagahama & Morino)
AGU & EGU: C2H6 (Mahieu et al.)
JpGU2018: CFCs (Takeda et al.)
IRWG2018: CFCs (Takeda et al., Nakajima et al),
HCN (Nagahama & Morino)
・ISEE workshop on detection of atmospheric composition change
with a ground-based infrared spectroscopy (held on 14-15 Nov. 2017)
14 talks + discussion on future plan of Japanese groups
The 20th anniversary symposium of Rikubetsu Observatory

## Slide 6: 20th anniversary symposium of Rikubetsu Observatory
held on November 8-9, 2017 at Rikubetsu town hall

## Slide 7: Issue of Rikubetsu FTIR
・Degrading spectrum in the filter #6 region since 2014
Since 2014, S/N of the spectrum in the filter #6 region has been
by 1/3-1/5 degraded in comparison with those obtained until 2010.
This may be caused by small intensity in the filter #6 region.
Due to degrading, retrievals of weak absorption lines such as
HNO3 and CFCs became difficult. For O3, DOFs and the total error
became worse significantly.
Currently, no data in HNO3 and ClONO2 since 2014 is archived
at NDACC DHF, although the O3 retrieval results are still archived.

## Slide 8
120M (-2010)
120/5HR (2014-)
(Courtesy of Masanori Takeda)
Spectra in the filter #6 region (In case of CFC-12)

## Slide 9: RMS and DOFs of O3 (1000-1005 cm-1)
120M
120/5HR

## Slide 10: Total error of retrieved total column from O3 (1000-1005 cm-1)

## Slide 11: Issue of Rikubetsu FTIR
・Degrading spectrum in the filter #6 region since 2014
Since 2014, S/N of the spectrum in the filter #6 region has been
by 1/3-1/5 degraded in comparison with those obtained until 2010.
This may be caused by small intensity in the filter #6 region.
Due to degrading, retrievals of weak absorption lines such as
HNO3 and CFCs became difficult. For O3, DOFs and the total error
became worse significantly.
Currently, no data in HNO3 and ClONO2 since 2014 is archived
at NDACC DHF, although the O3 retrieval results are still archived.

## Slide 12: Issue of Rikubetsu FTIR
・Degrading spectra in filter #6 region since 2014 (continued)
Some attempts to fix and improve the spectrum with filter #6 are
made, but the problem is not fixed yet (filter rotation, replacing
mirrors, …).
More challenges will be required in this year.
for hardware:
re-alignment, optimizing an aperture size, adjusting amplifier’s gain, …
for analysis:
co-adding spectra, …

## Slide 13: New mirrors of the solar tracker (further details appear in Morino’s poster)
Replaced on March, 2018

## Slide 14: Issue of Rikubetsu FTIR
・Degrading spectra in filter #6 region since 2014 (continued)
Some attempts to fix and improve the spectrum with filter #6 are
made, but the problem is not fixed yet (filter rotation, replacing
mirrors, …).
More challenges will be required in this year.
for hardware:
re-alignment, optimizing an aperture size, adjusting amplifier’s gain, …
for analysis:
co-adding spectra, …

## Slide 15: Future plan of ISEE/NU group
・Air quality monitoring in Nagoya using our 120HR (or 120M)
Why in Nagoya?
local pollutants in an urban area (many anthropogenic emissions)
continuous operation (hopeful)
lower operation cost (expected)
educational use (very important for young scientists)
validation with a new instrument (portable spectrometer, OSA, …)
We applied for some funds
(MEXT, JSPS, JST, …),
BUT failed in FY2018!
Now still seeking another fund.

## Slide 16: Summary
> NDACC measurements with the NIES Bruker 120/5HR are continued
at Rikubetsu. In the last 12 months, we measured in 32 days.
> Retrievals of vertical distribution of 12 species using SFIT4(v0.944)
until April 2018 are made, and are archived at the NDACC DHF.
> Degrading spectra in the filter #6 region appear since 2014. We tried
to fix this issue, but not yet. More challenges will be made!
> We have a plan to start measurement using our 120HR (or 120M) in
Nagoya for monitoring air quality in an urban area.

## Slide 17: Thank you!