## Slide 1
Thule & Mauna Loa (and Boulder) Site Report
Ivan Ortega & Jim Hannigan
Atmospheric Chemistry Observations & Modeling
National Center for Atmospheric Research

## Slide 2: Sites
76.53 ∘N, 291.26 ∘E
225 m.a.s.l
19.54 ∘N, 204.43 ∘E
3396 m.a.s.l
40.04 ∘N, 254.76 ∘E
1612 m.a.s.l
Boulder, Colorado
Mauna Loa, Hawaii
Thule, Greenland

## Slide 3: Thule & Mauna Loa: FTIR components

## Slide 4: Thule: High Arctic Atmospheric Observatory
- Danish Meteorological Institute (DMI) has left site
- NSF assumed site management with USAF
FTIR
Lidar – Tropospheric-Stratospheric Aerosol, Temperature
GMBS Ground-Based Millimeter-wave Spectrometer – Stratospheric CO, HNO3, N2O, O3
HATPRO microwave radiometer and Heitronics pyrometer –Tropospheric temperature profiles
The Vaisala DigiCora 2 sounding system - O3 & H2O sondes
water Vapor Emission Spectrometer for Polar Atmospheres at 22 GHz (VESPA-22) – Strat-Mesosphere
AERONET (solar, lunar AOD +)
Whole Sky Imager, Radiometers (IR, PAR, SW)
Room for more instrumentation
Current Suite of measurements
Balloon
Launch
AERONET/Radiometers
Main Lab
Lidar Hatch
Office
VESPA22 annex

## Slide 5: Thule: FTIR measurements
Number of dates with quality assured measurements
Installed 6” Au camera/ephemeris Solar Tracker in 2015
Installed a new 125HR in 2015
HR125 installed in May 2015
LN2 system installed in April 2017 (10 L/day)
2017: 2 visits; 117 days with QA spectra (record)
2018: so far 1 week visit (inclement weather)
Cryomech LNP10 LN2 generator installed in 2017

## Slide 6: Thule: HBr cell measurements/alignment
Shaded area represent roughly the limits from Sun et al. (2018) to suppress ILS sensitivity of TC of about 1%

## Slide 7: Thule: Summary SR
New FTIR 125HR, solar tracker and remote control components started in 2015 with improved feedback (instrument performing well)
2 site visits in 2017  LN2 system working good so far
117 polar days of QA measurements in 2017 (record)
So far 1 site visit in Feb 2018  start polar days; improved feedback
Standard gases are archived up to 2017 + some RD for CO, H2CO, CH4, O3 in 2018 (to be improved).
Danish Meteorological Institute left site  NSF manages now site logistics
Issues: oops!! N2O cell-#33 broke in 2018

## Slide 8: Mauna Loa: Kīlauea
Before May 2018
After May 2018
https://volcanoes.usgs.gov/volcanoes/kilauea/
Notes: May 6: A massive lava flow from the Kilauea volcano that broke out Sunday is destroying homes in the Leilani neighborhood of Hawaii’s Big Island.
The 2018 lower Puna eruption is an ongoing volcanic event on the island of Hawaiʻi on Kīlauea volcano's East Rift Zone that began on May 3, 2018. It is also part of the larger eruption of Kīlauea that began January 3, 1983, though some volcanologists and USGS scientists are considering whether to call it a new eruption.[2] Outbreaks of lava fountains up to 300 feet (90 m) high, lava flows and volcanic gas in the Leilani Estates subdivision were preceded by earthquakes and ground deformation that created cracks in the roads. The next day, May 4, a 6.9 magnitude earthquake hit Puna. After the initial outbreak, additional outbreaks of lava from new fissures in the Puna area occurred.

## Slide 9: Mauna Loa: FTIR measurements
Number of dates with quality assured measurements
2017: 2 visits; Upgraded to Windows/OPUS (1PC) and TCP data server (duplicate Thule)
2017: 282 days with QA spectra (record)
Evacuated, Kashiyama NeoDry 36e roots pump
NaCl window
120-125 Upgrade August 2011

## Slide 10: Mauna Loa: Summary SR
The acquisition components were upgraded at the end of 2017 (dedicated PC-Windows & Linux TCP server)  improved feedback.
Great NOAA technical support  LN2 and other minor issues.
282 days of QA measurements in 2017 (record)
Optimization of macro measurements was performed.
Standard gases are archived up to 2017 (except ClONO2) + some RD for CO, H2CO, CH4, O3 in 2018 (to be improved).
DU ‘Gondola’ dynamic tracker has been ok but a new solar tracker is desired (as Thule)  Limited funding
Early May 2018 Kilauea activity increased  might capture volcanic gasses (SO2, HCl, HF)

## Slide 11: Boulder: Update
Bruker 120HR started measurements in 2010
FTIR currently in Bruker for an upgrade  expected back in Boulder in August 2018
NDACC certification may start soon after upgrade
DU ‘Gondola’ dynamic tracker has been ok but a new solar tracker is desired (as Thule)  Limited funding
Bruker 120HR
Solar tracker

## Slide 12
OCS / IRWG  James Hannigan
  Network wide tropospheric/stratospheric OCS partial columns analysis
C2H6 / IRWG  Emmanuel Mahieu
  Recent focus on O&G exploration
  Network-wide trends + inversions + assimilations
H2CO / IRWG  Corinne Vigouroux
  Harmonization & TROPOMI validation
Supporting Arctic research (wildfires)  Erik Lutsch
N2O & HBr Cells / IRWG  Frank Hase
Temporal evolution of C2H6 to CO enhancement ratios, extended globally using MOPITT CO  Rebecca Buchholz/NCAR
SFIT4 updates; planning of new release
Projects 1: as part of NDACC

## Slide 13: On going projects at NCAR
Water vapor profiles
Oil and Natural Gas & feedlot emission factors derived from FTIR in Boulder (modeling component via GEOS-Chem, CAM-Chem & WRF-Chem)
OCS in Thule  Jim
Interested in NCAR/ACOM activities: ATOM
Tropospheric and lower stratospheric water vapor obtained with FTIR: comparison with balloon-borne FPH and influence on trace gas retrievals.
Evaluate the accuracy/precision of WV FTIR retrievals using coincident vertically resolved WV obtained within the past six years with balloon-borne NOAA Frost Point Hygrometers (FPH)
Quantify the impact of different a priori.
study the influence of different sources of WV profiles in the retrieval of selected gas profiles.
(1)
Long-term variability and source signature from oil & natural gas and feedlot operations in the Colorado Front range
Characterize source signature of seven years of FTIR measurements in Boulder, Colorado.
Estimate emission factors related to O&NG/feedlot operations.
Evaluate Chemistry models (CAM-Chem, Geos-Chem)
(2)
Others: Water vapor isotopologues, rapid change in the Arctic, NCAR/ACOM activities
(3)
Poster

## Slide 14: Publications: 2017 - present
Tropospheric ozone assessment report: Present-day distribution and trends of tropospheric ozone relevant to climate and global atmospheric chemistry model evaluation. Elementa: Science of the Anthropocene. Gaudel, A., and Coauthors, 2018:
The Network for the Detection of Atmospheric Composition Change (NDACC): History, status and perspectives. ACP. De Mazière, M., and Coauthors, 2018
Discovery of new coronal lines at 2.843 and 2.853 μm. The Astrophysical Journal, Samra, J. E., P. G. Judge, E. E. DeLuca, and J. W. Hannigan, 2018
MLS measurements of stratospheric hydrogen cyanide during the 2015-2016 El Niño event. ACP. Pumphrey, H. C., and Coauthors, 2018
Comparison of the GOSAT TANSO-FTS TIR CH volume mixing ratio vertical profiles with those measured by ACE-FTS, ESA MIPAS, IMK-IAA MIPAS, and 16 NDACC stations. AMT. Olsen, K. S., and Coauthors, 2017
The CU mobile Solar Occultation Flux instrument: structure functions and emission rates of NH3, NO2 and C2H6. Kille et al., Atmos. Meas. Tech., 10, 373-392, doi:10.5194/amt-10- 373-2017, 2017.
Reference Upper-Air Observations for Climate: From Concept to Reality. G. E. Bodeker, S. Bojinski, D. Cimini, R. J. Dirksen, M. Haeffelin, J. W. Hanni- gan, D. F. Hurst, T. Leblanc, F. Madonna, M. Maturilli, A. C. Mikalsen, R. Philipona, T. Reale, D. J. Seidel, D. G. H. Tan, P. W. Thorne, H. V ̈omel and J. Wang. Bulletin of the American Meteorological Society, 97(1):123–135, 2016. doi:10.1175/BAMS-D-14-00072.1.
Validation of MOPITT carbon monoxide using ground-based Fourier trans- form infrared spectrometer data from NDACC. R. R. Buchholz, M. N. Deeter, H. M. Worden, J. Gille, D. P. Edwards, J. W. Hannigan, N. B. Jones, C. Paton-Walsh, D. W. T. Griffith, D. Smale, J. Robinson, K. Strong, S. Con- way, R. Sussmann, F. Hase, T. Blumenstock, E. Mahieu and B. Langerock. Atmospheric Measurement Techniques Discussions, 2016:1–44, 2016. doi:10.5194/amt-2016-241.
An evaluation of IASI-NH3 with ground-based Fourier transform infrared spectroscopy measurements. E. Dammers, M. Palm, M. Van Damme, C. Vigouroux, D. Smale, S. Conway, G. C. Toon, N. Jones, E. Nussbaumer, T. Warneke, C. Petri, L. Clarisse, C. Clerbaux, C. Hermans, E. Lutsch, K. Strong, J. W. Hannigan, H. Nakajima, I. Morino, B. Herrera, W. Stremme, M. Grutter, M. Schaap, R. J. Wichink Kruit, J. Notholt, P.-F. Coheur and J. W. Eris- man. Atmospheric Chemistry and Physics, 16(16):10351–10368, 2016. doi: 10.5194/acp-16-10351-2016.
Validation of the CrIS Fast Physical NH3 Retrieval with ground-based FTIR. Dammers, E. et al., in review. Atmospheric Measurement Techniques, 2017.
Acknowledgments
The measurements and analysis are performed with contract support from NASA.
NCAR is supported by the National Science Foundation.
We are grateful to the NOAA staff at MLO & DMI/new staff at Thule for technical support and maintenance of the NCAR FTIR.
!THANKS!