## Slide 1
IRWG / TCCON Meeting, Mexico, June 11 – June 15, 2018
BIRA-IASB sites report
TCCON site @ St. Denis, Ile de La Réunion
NDACC-IRWG site @ Maïdo, Ile de La Réunion
NDACC-IRWG site @ Porto Velho, Brazil
Mahesh Kumar Sha, Bavo Langerock, Corinne Vigouroux, Christian Hermans, Nicolas Kumps, Francis Scolas, Minqiang Zhou, Martine De Mazière (PI)
Royal Belgian Institute for Space Aeronomy, Belgium
Jean-Marc Metzger, Valentin Duflot, Jean-Pierre Cammas
Université de la Réunion, France
Carlos Augusto Bauer Aquino (IFRO), Christiane Silvestrini de Morais (IFRO), Luciana Vanni Gatti (CCST/INPE)
Brazil

## Slide 2
Ile de La Réunion (21° S, 55° E)
An unique atmospheric observatory situated in the Indian Ocean, about 700 km east of Madagascar and 170 km southwest of Mauritius providing the background state. In addition, we see the influence of biomass burning in Madagascar, South Africa and South America
One of the very few atmospheric observation stations providing both in-situ and remote sensing greenhouse gas (GHG) data for atmospheric components in the southern hemisphere
Two dedicated sites – St. Denis (85 m.a.s.l) and Maïdo (2157 m.a.s.l)
Google Earth
St. Denis
Maïdo
Ile de la Réunion

## Slide 3
Instrumentation at St. Denis, Ile de La Réunion
Location: University of St. Denis (-20.901° N, 55.485° E, 85 m.a.s.l)
Instrument characteristics: Bruker IFS 125HR, CaF2 Beamsplitter and optics, home-built sun-tracker and electronics
Networks: TCCON (InGaAs and Si) and NDACC (InSb) (since September 2011)
Sun tracker for the Bruker IFS 125HR
FTIR spectrometer – Bruker IFS 125HR

## Slide 4
Instrumental line shape parameters at St. Denis
Diagnostic parameters for checking the instrument performance

## Slide 5
Instrumental line shape parameters at St. Denis
Diagnostic parameters for checking the instrument performance

## Slide 6
Instrumental line shape parameters at St. Denis
Diagnostic parameters for checking the instrument performance

## Slide 7
SNR plot for measurements at St.Denis
Suntracker problem
Electricity works on the building
Acquizition card problem
Change of PC
Storm warning
Rain detector failure
Few gaps in the timeseries due to solartracker problem, maintenance work at the site, storm warning and PC problem
a.u.
a.u.

## Slide 8
FTIR measurement statistics at St. Denis

## Slide 9
St. Denis TCCON time series
Time series of few selected GHG
Completed 6 years of TCCON measurements
Data available on TCCON public database 3 months after the measurements
RD data also available upon request
e.g.: RD data is currently used for CAMS84 and TCCON4S5P
Visualize our data here: http://infrared-data.aeronomie.be/

## Slide 10
Instrumentation at Maïdo
Location: Maïdo observatory (-21.079° N, 55.384° E, 2157.7 m.a.s.l)
Instrument characteristics: Bruker IFS 125HR, KBr Beamsplitter and optics, home-built sun-tracker and electronics
Networks: NDACC (InSb and HgCdTe) and TCCON (InGaAs) (since March 2013)
Maïdo observatory
FTIR spectrometer – Bruker IFS 125HR

## Slide 11
Instrumental line shape parameters at Maido
Diagnostic parameters for checking the instrument performance

## Slide 12
SNR plot for measurements at Maïdo
Power supply failure
Storm warning
No instrumental problem during the last year, few gaps in the timeseries due to liquid nitrogen delivery delay, storm warning and power failure.
a.u.
Change of hard drive

## Slide 13
FTIR measurement statistics at Maïdo

## Slide 14
Maïdo NDACC time series
Submission of standard NDACC species as usual.
New species “N2O” submitted to NDACC

## Slide 15
Our new site in Brazil – @ Porto Volho
Site location: Porto Velho – in the amazon forest in Brazil
Laboratory constructed for hosting our Bruker spectrometer
Instrument installed and running since 15 July 2016
We plan to start TCCON like measurements of GHGs in the NIR soon at Porto Velho.
Porto Velho

## Slide 16
Instrumentation at Porto Velho
Location: Porto Velho (-8.774° N, 296.128° E, 87.0 m.a.s.l)
Instrument characteristics: Bruker IFS 125M (upgraded St. Denis Bruker IFS 120M spectrometer)
KBr/CaF2 Beamsplitter and optics, home-built sun-tracker and electronics, fully automatic operation
Networks: NDACC (currently – InSb detector only, very soon we will install – HgCdTe detector)
Homemade solar tracker
FTIR spectrometer – Bruker IFS 125M
Meteostation

## Slide 17
Instrumental line shape parameters at Porto Velho
Diagnostic parameters for checking the instrument performance

## Slide 18
SNR plot for measurements at Porto Velho
Interferometer drive problem
Suntracker problem: E motor
Measurements started with InSb detector on 15/07/2016
Interferometer drive problem: 20/07/2017
- Waiting for Bruker site visit for analysis and solving of the problem
a.u.

## Slide 19
Porto Velho time series
Time series extended from what was shown during the last meeting.
Data not yet submitted to NDACC
For retrieval results contact:
Corinne Vigouroux corinne.vigouroux@aeronomie.be or
Bavo Langerock bavo.langerock@aeronomie.be or
Minqiang Zhou minqiang.zhou@aeronomie.be

## Slide 20
FTIR measurement statistics at Porto Velho

## Slide 21
In-situ and FTIR joint data usage

## Slide 22
Publication list since last meeting
Vigouroux, C. et al.: NDACC harmonized formaldehyde time-series from 21 FTIR stations covering a wide range of column abundances, Atmos. Meas. Tech. Discuss., https://doi.org/10.5194/amt-2018-22, in review, 2018.
Gaudel A, et al. . Tropospheric Ozone Assessment Report: Present-day distribution and trends of tropospheric ozone relevant to climate and global atmospheric chemistry model evaluation, Elem Sci Anth .; 6 ( 1 ) :39 . DOI: http://doi.org/10.1525/elementa.291, 2018.
Chabrillat, S., Vigouroux, C., Christophe, Y., Engel, A., Errera, Q., Minganti, D., Monge-Sanz, B. M., Segers, A., and Mahieu, E.: Comparison of mean age of air in five reanalyses using the BASCOE transport model, Atmos. Chem. Phys. Discuss., https://doi.org/10.5194/acp-2018-354, in review, 2018.
Zhou, M., Langerock, B., Vigouroux, C., Wang, P., Hermans, C., Stiller, G., Walker, K. A., Dutton, G., Mahieu, E., and De Mazière, M.: Ground-based FTIR retrievals of SF6 on Reunion Island, Atmos. Meas. Tech., 11, 651–662, doi:10.5194/amt-11-651-2018, 2018.
De Mazière, M., Thompson, A. M., Kurylo, M. J., Wild, J. D., Bernhard, G., Blumenstock, T., Braathen, G. O., Hannigan, J. W., Lambert, J.-C., Leblanc, T., McGee, T. J., Nedoluha, G., Petropavlovskikh, I., Seckmeyer, G., Simon, P. C., Steinbrecht, W., and Strahan, S. E.: The Network for the Detection of Atmospheric Composition Change (NDACC): history, status and perspectives, Atmos. Chem. Phys., 18, 4935-4964, https://doi.org/10.5194/acp-18-4935-2018, 2018.
Zhou, M., Langerock, B., Vigouroux, C., Sha, M. K., Ramonet, M., Delmotte, M., Mahieu, E., Bader, W., Hermans, C., Kumps, N., Metzger, J.-M., Duflot, V., Wang, Z., Palm, M., and De Mazière, M.: Atmospheric CO and CH4 time series and seasonal variations on Reunion Island from ground-based in-situ and FTIR (NDACC and TCCON) measurements, Atmos. Chem. Phys. Discuss., https://doi.org/10.5194/acp-2018-218, in review, 2018.

## Slide 23
Publication list since last meeting
Lianghai Wu, Otto Hasekamp, Haili Hu, Jochen Landgraf, Andre Butz, Joost aan de Brugh, Ilse Aben, Dave F. Pollard, David W. T. Griffith, Dietrich G. Feist, Dmitry Koshelev, Frank Hase, Geoffrey C. Toon, Hirofumi Ohyama, Isamu Morino, Justus Notholt, Kei Shiomi, Laura Iraci, Matthias Schneider, Martine de Mazière, Ralf Sussmann, Rigel Kivi, Thorsten Warneke, Tae-Young Goo, and Yao Té, Carbon dioxide retrieval from OCO-2 satellite observations using the RemoTeC algorithm and validation with TCCON measurements, Atmos. Meas. Tech., 11, 3111-3130, https://doi.org/10.5194/amt-11-3111-2018, 2018
De Wachter, E., Kumps, N., Vandaele, A. C., Langerock, B., and De Mazière, M.: Retrieval and validation of MetOp/IASI methane, Atmos. Meas. Tech., 10, 4623-4638, https://doi.org/10.5194/amt-10-4623-2017, 2017.
Sun, Y., Liu, C., Palm, M., Vigouroux, C., Hu, Q., Tian, Y., Wang, W., Su, W., Zhang, W., Shan, C., Xu, X., Liu, J., Notholt, J., and De Mazière, M.: Ozone seasonal evolution and photochemical production regime in polluted troposphere in eastern China derived from high resolution FTS observations, Atmos. Chem. Phys. Discuss., https://doi.org/10.5194/acp-2017-1176, in review, 2017.
Steinbrecht, et al.: An update on ozone profile trends for the period 2000 to 2016, Atmos. Chem. Phys., 17, 10675-10690, https://doi.org/10.5194/acp-17-10675-2017, 2017.
Duflot, V., Baray, J.-L., Payen, G., Marquestaut, N., Posny, F., Metzger, J.-M., Langerock, B., Vigouroux, C., Hadji-Lazaro, J., Portafaix, T., De Mazière, M., Coheur, P.-F., Clerbaux, C., and Cammas, J.-P.: Tropospheric ozone profiles by DIAL at Maïdo Observatory (Reunion Island): system description, instrumental performance and result comparison with ozone external data set, Atmos. Meas. Tech., 10, 3359-3373, https://doi.org/10.5194/amt-10-3359-2017, 2017.

## Slide 24
Publication list since last meeting
Kevin S. Olsen, Kimberly Strong, Kaley A. Walker, Chris D. Boone, Piera Raspollini, Johannes Plieninger, Whitney Bader, Stephanie Conway, Michel Grutter, James W. Hannigan, Frank Hase, Nicholas Jones, Martine de Mazière, Justus Notholt, Matthias Schneider, Dan Smale, Ralf Sussmann, and Naoko Saitoh, Comparison of the GOSAT TANSO-FTS TIR CH volume mixing ratio vertical profiles with those measured by ACE-FTS, ESA MIPAS, IMK-IAA MIPAS, and 16 NDACC stations, Atmos. Meas. Tech., 10, 3697-3718, https://doi.org/10.5194/amt-10-3697-2017, 2017
Tobias Borsdorff, Joost aan de Brugh, Haili Hu, Otto Hasekamp, Ralf Sussmann, Markus Rettinger, Frank Hase, Jochen Gross, Matthias Schneider, Omaira Garcia, Wolfgang Stremme, Michel Grutter, Dietrich G. Feist, Sabrina G. Arnold, Martine De Mazière, Mahesh Kumar Sha, David F. Pollard, Matthäus Kiel, Coleen Roehl, Paul O. Wennberg, Geoffrey C. Toon, and Jochen Landgraf, Mapping carbon monoxide pollution from space down to city scales with daily global coverage, Atmos. Meas. Tech. Discuss., https://doi.org/10.5194/amt-2018-132, in review, 2018

## Slide 25
Funding dedicated for maintenance of NDACC and TCCON infrastructure, ‘routine’ observations & data analysis
    Limited institute support (~ 1 FTE + <30 kEuro/yr)
    Limited support for TCCON and ICOS in-situ observations via national contribution to ICOS (2018-2019) of order 65 kEuro/year for 2018 and 2019
    support for Porto Velho via IKARE (Improving Knowledge of the Amazon Rainforest Emissions ) national research project is coming to an end; no perspective for a new project at present
Funding dedicated to progress in TCCON data analysis and delivery
    EU RI project RINGO
     compliance of La Reunion TCCON data with ICOS requirements and vertical profiling studies
    FRM4GHG – phase 2 (March 2018 – February 2019)  dedicated campaign (see talk by M. De Mazière)
  No funding dedicated to progress in NDACC data analysis and delivery
Funding situation / projects

## Slide 26
Funding dedicated to use of existing (RD & public) NDACC/TCCON observations
    Prodex TROVA (2016-2018)  validation of S5P (TROPOMI): continuation for next 3 years must be negotiated
    S5P-Mission Performance Center (2016-2021)  operational validation of S5P using all available Fiducial Reference Measurements (incl. NDACC & TCCON)
    CAMS-84 (2016-2018)  validation of CAMS analyses and forecasts using selected NDACC data: continuation until 2021 is under negotiation
    CAMS-27 (2017-2021)  very limited funding for QA/QC of NDACC data stream for CAMS-84
    ESA-CCI+ GHG project (2018-2021)  limited continuation of validation of satellite GHG data using TCCON data; proposal in preparation
    C3S-BARON (C3S_311a_Lot3, 2017-2020): support for harmonisation and delivery of NDACC O3, CH4 and CO data and associated ancillary data to Copernicus Climate Change Service (C3S) Climate Data Store
Funding situation / projects

## Slide 27
Thank you for your attention