## Slide 1: The University of Toronto Atmospheric Observatory: Site Report
Kimberly Strong, Shoma Yamanouchi, Brendan Byrne, Orfeo Colebatch, Erik Lutsch, Sebastien Roche, Lei Liu, Stephanie Conway, Alistair Duff
Department of Physics, University of Toronto
NDACC IRWG Meeting
Mexico
13 June 2018

## Slide 2: University of Toronto Atmospheric Observatory: TAO
43.66N, 79.40 W, 174 m asl
Primary instrument: Bomem DA8 FTIR
  Coupled to Community Solar Tracker (pointing accuracy of 10-20 arc seconds, 0.0028°)
  Semi-automated MIR measurements
  Can be remotely accessed/operated
  Columns and vertical profiles retrieved using the SFIT4 algorithm
Additional instruments:
  ECCC Brewer (on loan 2005-2016)
  ECCC Pandora UV-visible spectrometer for O3, NO2, O4, HCHO, HONO, etc. (#109 Nov 2016 – May 2018, #145 since 15/5/2018)
  Weather station (Davis Vantage Pro 2 Plus, and Vaisala PTU300)
Photo: Cyndi Whaley

## Slide 3: TAO FTIR Measurements
October 2001 – Bomem DA8 operational
May 2002 to present – regular solar measurements
March 2004 – NDACC certification

## Slide 4: Status of NDACC Data Submission
Most recent (sixth) archiving: March 2017
  Data until the end of 2016 was uploaded in March 2017
  Analyzed with SFIT4 V0.9.4.4, and formatted as HDF
  O3, CO, CH4, N2O, C2H2, CH3OH, H2CO, HCl, HCN, HCOOH, HF, HNO3, NH3
  Planning to archive 2017 NDACC data this summer
  Began archiving CO, CH4, and O3 for CAMS Rapid Delivery in March 2018
Previous (fifth) archiving: June 2015
  Reanalyzed data set (2002-2014) using SFIT4 V0.9.4.4 with full error analysis, SNR calculated from spectra, optimized retrieval strategy
  O3, HCl, HF, HNO3, N2O, CH4, CO, HCN, C2H6
Older archiving events
  Fourth archiving in October 2013
    Reanalyzed the complete data set (2002-2012) and submitted in HDF format: O3, HCl, HF, N2O, CH4, CO, HCN, C2H6
    Used SFIT4 V0.9.4.1, HITRAN 2008, IRWG recommended microwindows, WACCM v6, random error for each retrieval, average systematic errors
  Earlier archiving used SFIT2 and NASA Ames format: 2005, 2007, 2010

## Slide 5: TAO FTIR Time Series: 2002-2016
Total columns
Aldona Wiacek,
Jeff Taylor,
Cyndi Whaley,
Ilya Stanevich,
Stephanie Conway,
Orfeo Colebatch
and many others
Plot: Shoma Yamanouchi
Stephanie and Erik reanalyzed the FTIR dataset for 2002-2016 using SFIT4 V0.9.4.4

## Slide 6: HBr Instrument Line Shapes
HBr cell #48, measured on 20 February 2018
  100 scan HBr, 0.004 cm-1, filter 3
  Background: Norton-Beer strong apodization, 0.01 cm-1, filter 3
  Analyzed with LINEFIT v14.5
  ILS measurements were updated to 100 scan + low-resolution background in February-March 2017

## Slide 7: HBr Instrument Line Shapes

## Slide 8: Retrieved HBr Cell Columns

## Slide 9: TAO Activities over the Past Year
Measurements
  Semi-automated daily measurements with remote desktop functionality
  Generating daily summary reports showing FTIR spectra, sun-tracking, solar radiation and weather conditions
Research
  Shoma Yamanouchi (see talk) – biomass burning, trend analysis
  Erik Lutsch – data analysis for CAMS RD and TROPOMI
  Erik, Shoma, Stephanie Conway – TAO retrievals (ESSD in prep.)
  Kevin Olsen – GOSAT TIR CH4 validation (AMT 2017)
  Brendan Byrne – long-path measurements with Bruker 125M
Contributions to other studies
  Whitney Bader – NDACC CH4 trends (ACP 2017)
  Enrico Dammers – CrIS NH3 validation (AMT 2017)
  Rebecca Buchholz – MOPITT CO validation (AMT 2017)
  Corinne Vigouroux – NDACC HCHO time series (AMT submitted)
  Zitely Tzompa-Sosa – C2H6 emissions (JGR 2017 and JGR submitted)

## Slide 10: Open-Path FTIR
https://uoftlongpath.wordpress.com/
Bruker 125M with telescope and retroreflector from ECCC
Testing open-path operation with initial focus on CO2, CO, CH4 and N2O in downtown Toronto
Brendan Byrne, Orfeo Colebatch

## Slide 11: UofT OP-FTIR Time Series
Brendan Byrne, Orfeo Colebatch
Retrievals with MALT software
Investigating sensitivity to meteorology
Comparing with in situ data

## Slide 12: Outlook & Future Work
Ongoing DA8 measurements, analysis, interpretation
125M OP-FTIR operations and retrievals
Integration of measurements and modelling (GEOS-Chem) in collaboration with Dylan Jones (UofT)
Comparison of urban (TAO) and rural (ECCC Egbert) FTIR measurements
Funding
  Natural Sciences and Engineering Research Council of Canada (NSERC)
  Canadian Space Agency (CSA)
  University of Toronto

## Slide 13: Eureka Site Report
NDACC IRWG Meeting
Mexico
13 June 2018
Kimberly Strong, Erik Lutsch, Dan Weaver, Pierre Fogal, Sebastien Roche, Lei Liu, Stephanie Conway, Tyler Wizenberg
Department of Physics, University of Toronto

## Slide 14: The PEARL at Eureka
Polar Environment Atmospheric Research Laboratory
  Run by the Canadian Network for Detection of Atmospheric Change (CANDAC) since August 2005
  ~25 experiments at 3 facilities
Located on Ellesmere Island, Nunavut (80°N, 86°W, 610m)
15 km from Env. Canada’s Eureka Weather Station
1100 km from North Pole

## Slide 15: PEARL 125HR History
Installed July 2006; mid-IR configuration
NDACC certification February 2009
Replaced Bomem DA8 – removed in 2009
Joined TCCON June 2010; alternating mid-IR and near-IR
Intensive campaigns
  Canadian Arctic ACE/OSIRIS Validation Campaigns: 2007  2018
  July 2007 – Bomem DA8 intercomparison
Upgrades and maintenance
  August-September 2009 – NIR upgrade
  July 2010 – Relocation of 125HR
  July 2013 – New Community Solar Tracker and Robodome installed
  February 2015 – New computer installed
  July 2015 – Laser replaced with SIOS
  February 2016 – First N2O cell tests
  March 2017 – Alignment of 125HR
  March 2018 – Exit flat mirror adjustment
Measurement days (MIR and/or NIR):
  2006: 17
  2007: 117
  2008: 121
  2009: 111
  2010: 92
  2011: 85
  2012: 30
  2013: 27
  2014: 106
  2015: 144
  2016: 115 (99 MIR, 89 NIR)
  2017: 102 (67 MIR, 62 NIR)
  2018 to date: 77 (61 MIR, 46 NIR)

## Slide 16
Canadian Arctic ACE/OSIRIS Validation Campaign Measurements
Collected 2361 solar measurements during the 2018 ACE campaign over 26 days between 27 February and 1 April.
        1185 MIR (22 days)
        1176 NIR (13 days)
Chart: Bruker 125HR measurements
| 43158 | 43159 | 43160 | 43161 | 43162 | 43163 | 43164 | 43165 | 43166 | 43167 | 43168 | 43169 | 43170 | 43171 | 43172 | 43173 | 43174 | 43175 | 43176 | 43177 | 43178 | 43179 | 43180 | 43181 | 43182 | 43183 | 43184 | 43185 | 43186 | 43187 | 43188 | 43189 | 43190 | 43191
MIR | 2 | 2 | 0 | 0 | 0 | 0 | 26 | 24 | 63 | 0 | 0 | 111 | 57 | 41 | 0 | 0 | 58 | 42 | 38 | 45 | 0 | 40 | 111 | 4 | 31 | 0 | 0 | 81 | 22 | 2 | 110 | 117 | 158 | 0
NIR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 167 | 184 | 0 | 0 | 101 | 0 | 0 | 79 | 94 | 125 | 41 | 0 | 0 | 0 | 0 | 78 | 0 | 90 | 33 | 100 | 15 | 0 | 0 | 0 | 69
See poster: Strong, Walker et al.

## Slide 17: Bruker 125HR Line Shape: MIR N2O
Spring 2018 tests with 180 cm MOPD
180227 (yellow): ME ~0.8, typical since March 2017 alignment improved the NIR ILS but degraded the MIR ILS. Used the usual 1.15 mm aperture.
180313 (first 3): ME ~0.9, after adjusting the flat mirror before the exit aperture. Used the usual 1.15 mm aperture.
180306, 180312, 180313 (4th): ME ~1, all done with 1 mm aperture (used for NIR HCl) – indicates aperture issue

## Slide 18: Bruker 125HR Line Shape: NIR HCl
Spring 2018 tests with 45 cm MOPD
1.00 < ME < 1.04 since alignment in March 2017
180308 (blue): with 1.15 mm aperture (standard for N2O/HBr tests) – indicates aperture issue
All others with 1 mm aperture (standard for HCl)
180312 (grey): after the exit mirror adjustment, ME with 1 mm aperture seems unchanged.
Phase error close to 0.
180611 (pink): current

## Slide 19: Status of NDACC Data Submission
Most recent (fifth) archiving: March 2017
  Data until the end of 2016 was uploaded in March 2017
  Analyzed with SFIT4 V0.9.4.4, and formatted as HDF
  O3, CO, CH4, N2O, C2H2, CH3OH, H2CO, HCl, HCN, HCOOH, HF, HNO3, NH3
  Planning to archive 2017 NDACC data this summer
  Began archiving CO, CH4, and O3 for CAMS Rapid Delivery in March 2018
  TCCON archiving has been delayed while assessing sun-tracker SZA corrections – reprocessing almost done, will upload full dataset very soon
Fourth archiving: June 2015
  Reanalyzed data set (2006-2014) using SFIT4 V0.9.4.4 with full error analysis, SNR calculated from spectra, updated retrieval schemes, and addressed some issues with a priori profiles
  O3, HCl, HF, HNO3, ClONO2, N2O, CH4, CO, HCN, C2H6
Third archiving: October 2013
  Reanalyzed the complete data set (August 2006 – April 2013), HDF format
  O3, HCl, HF, HNO3, ClONO2, CO, N2O, CH4, HCN, C2H6
  SFIT4 V0.9.4.1, HITRAN 2008, IRWG microwindows, WACCM v6, random error for each retrieval, average systematic errors
First two archivings
  SFIT2 v3.92c, HITRAN 2004 + updates, NASA Ames
  O3, HCl, HF, ClONO2, HNO3, N2O, CO, CH4
  September 2010 and October 2012

## Slide 20: PEARL FTIR Time Series: 2006-2016
Total columns
Stephanie and Erik have reanalyzed the FTIR dataset (2006-2016) using SFIT4 V0.9.4.4
Stephanie Conway, Erik Lutsch, Dan Weaver, Joseph Mendonca, Sebastien Roche, Camille Viatte, Rodica Lindenmaier, Rebecca Batchelor

## Slide 21: Activities Over the Past Year
Running with a combination of remote operation and on-site operator, alternating MIR and NIR measurements
Erik Lutsch – biomass burning studies (see two talks); data analysis for CAMS RD and TROPOMI
Sebastien Roche – TCCON analysis and CO2 profiling (see TCCON talk)
Lei Liu – trace gas retrievals and cloud studies using AERI emission spectra (see talk)
Kaley Walker and team – ACE/OSIRIS validation (see poster)
Dan Weaver – H2O intercomparisons with MUSICA data
Xiaoyi Zhao – surface ozone & HDO depletion with MUSICA data
Whitney Bader – retrieval strategy for CH3D and 13CH4
Ralf Bauer, Stephanie Conway – CFCs & HCFCs

## Slide 22: PEARL H2O Intercomparisons using MUSICA
Since 2017 IRWG meeting:
First paper published in AMT
Profile comparisons became separate paper – will soon be submitted to AMT
Dan Weaver
Radiosondes (GRUAN)
125HR (MUSICA product)
ACE-FTS & ACE-MAESTRO (on SCISAT-1/ACE)
MIPAS & SCIAMACHY (on ENVISAT)
AIRS (on Aqua)
MLS & TES (on Aura)

## Slide 23: NDACC Publications
Barthlott et al., Tropospheric water vapour isotopologue data (H216O, H218O and HD16O) as obtained from NDACC/FTIR solar absorption spectra. Earth System Science Data, 2017.
Buchholz et al., Validation of MOPITT carbon monoxide using ground-based Fourier transform infrared spectrometer data from NDACC. Atmos. Meas. Tech., 2017.
Strong, Lutsch, and Zhao, Using ground-based UV-VIS-IR spectroscopy to probe atmospheric composition over Canada. Physics in Canada special issue on Remote Sensing of the Atmosphere, invited, 2017.
Griffin, Walker et al., Multi-year comparisons of ground-based and space-borne Fourier Transform Spectrometers in the high Arctic between 2006 and 2013. Atmos. Meas. Tech., August 2016.
Weaver et al., Intercomparison of atmospheric water vapour measurements in the Canadian high Arctic. Atmos. Meas. Tech., 2017.
Dammers et al., Validation of the CrIS Fast Physical NH3 Retrieval with ground-based FTIR. Atmos. Meas. Tech., 2017.
Zhao, Strong et al., Cyclone-Induced Surface Ozone and HDO Depletion in the Arctic. Atmos. Chem. Phys., May 2017.
Vigouroux et al., NDACC harmonized formaldehyde time-series from 21 FTIR stations covering a wide range of column abundances. Atmos. Meas. Tech. Discuss., in review, 2018.

## Slide 24: TCCON / GHG Publications
Belikov et al., Study of the footprints of short-term variation in XCO2 observed by TCCON sites using NIES and FLEXPART atmospheric transport models. Atmos. Chem. Phys., 2017.
Bader et al., The recent increase of atmospheric methane from 10 years of ground-based NDACC FTIR observations since 2005. Atmos. Chem. Phys., 2017.
Mendonca et al., Using high-resolution laboratory and ground-based solar spectra to assess CH4 absorption coefficient calculations. JQSRT, 2017.
Tzompa-Sosa et al., Revisiting global fossil fuel and biofuel emissions of ethane, J. Geophys. Res. Atmos., 2017.
Feng et al., Consistent regional fluxes of CH4 and CO2 inferred from GOSAT proxy XCH4:XCO2 retrievals, 2010-2014. Atmos. Chem. Phys., 2017.
Wunch et al., Comparisons of the Orbiting Carbon Observatory-2 (OCO-2) XCO2 measurements with TCCON, Atmos. Meas. Tech., 2017.
Byrne, Jones, Strong et al., Sensitivity of CO2 surface flux constraints to observational coverage, J. Geophys. Res. Atmos., 2017.
Olsen, Strong et al., Comparison of the GOSAT TANSO-FTS TIR CH4 volume mixing ratio vertical profiles with those measured by ACE-FTS, ESA MIPAS, IMK-IAA MIPAS, and 16 NDACC stations, Atmos. Meas. Tech., 2017.
Mendonca et al., Improving the Retrieval of XCO2 from Total Carbon Column Network Solar Spectra. Atmos. Meas. Tech. Discuss., in review, 2018.

## Slide 25: Funding Outlook for PEARL
NSERC’s Climate Change and Atmospheric Research Program (2013-2018): Probing the Atmosphere of the High Arctic (PAHA) – “Save PEARL” campaign resulted in 18 month extension to Sept 2019
CSA support for AVATARS – Arctic Validation And Training for Atmospheric Research in Space (2016-2019): one year left
CSA support for the Canadian Arctic ACE/OSIRIS Validation Campaign project (2018-2022) led by Kaley Walker: new funding for four more spring campaigns
NSERC support for “Operations and Maintenance Support for the Polar Environment Atmospheric Research Laboratory (PEARL)” (2017-2019): one year left

## Slide 26: Acknowledgements
We gratefully acknowledge support from the following:
PEARL/CANDAC (http://www.candac.ca)
ARIF, AIF/NSRIT, CFCAS, CFI, CSA, ECCC, GOC-IPY, INAC, MRI, MSC, NSERC, NSTP, OIT, ORF, PCSP, SEARCH
PI Jim Drummond, Site Manager Pierre Fogal
ACE Arctic Validation Campaigns (https://eureka.physics.utoronto.ca)
CSA, ECCC, NSERC, NSTP
Co-PI Kaley Walker
Logistical and operational support at Eureka
The wonderful team at the ECCC Weather Station
The CANDAC operators