## Slide 1: Spectroscopy Update
A major event in 2017 was the release of HITRAN2016. This happens every 4 years only, and so merits serious attention.
A lot of work evaluating HITRAN 2016. I have so far looked at H2O, CO2, O3. Next up is N2O.
As usual with HITRAN, the new release represents 2 steps forward, one step backward.
Today I will show my CO2 evaluation as example of the methodology. This is the main thrust of today’s talk.
No time to show O3 or H2O, but you can read the O3 report here:
https://mark4sun.jpl.nasa.gov/report/o3_spectroscopy_evaluation_20170930.compressed.pdf
On a completely separate topic, pseudo-linelists have been created for:
CFH2CF3 (HFC-134a): https://mark4sun.jpl.nasa.gov/data/spec/Pseudo/HFC-134a_PLL.compressed.pdf
CH3COCH3 (Acetone): https://mark4sun.jpl.nasa.gov/data/spec/Pseudo/CH3COCH3_PLL.compressed.pdf
C3H6 (Propene): “FTIR Measurements of Mid-IR Propene (C3H6) cross-sections at temperatures between 150 and 299 K”, Sung, Toon et al., JQSRT, 213 (2018), 119-132

## Slide 2: New PLLs

## Slide 3: CFH2CF3 (HCF-134a) PLLs
The CFH2CF3 PLL was one of the most interesting & ambitious PLLs that I have ever attempted. Six different sets of lab cross-sections were fitted simultaneously, all covering different wavenumbers, spectral resolutions, temperature, pressures, vmrs, path lengths, and all with their own idiosyncracies and biases. But it all converged in the end.

## Slide 4: CFH2CF3 Retrieved VSFs using PLL
Showing VSFs averaged over all 12 windows. 103 lab spectra in total. Over 400 spectral fits.
All VSFs within 5% of 1.00.

## Slide 5: CO2 Spectroscopy Evaluation
Various CO2 linelists, old and new, have been evaluated using lab (mainly Kitt Peak) and solar absorption (MkIV, TCCON) spectra.
Linelist were evaluated in terms of their rms spectral fits, and the consistency of the retrieved gas amounts between different windows.
A set of wide windows covering 650 to 7000 cm-1 was defined, encompassing all the detectable CO2 bands,
GFIT spectral fitting code was used, assuming a Voigt lineshape and no LM. Except in two window where fits were made with and without LM to gauge sensitivity.
All CO2 isotopologs were fitted together. No attempt to obtain separate evaluations for each.
That said, some of the Kitt Peak lab spectra were 13C-enriched.
A new linelist is being generated by combining the best aspects of previous HITRAN version, together with a few ad hoc empirical corrections (“HITRAN CO2’s Greatest Hits”)

## Slide 6: CO2 Linelists Evaluated
HIT08: 314,919 lines
HIT12: 471,847 lines
ATM16: 450,493 lines: Mostly HITRAN 2012. Based on Toth (2008) for the the 5740-6600 cm-1 region because it gave better fits. Empirical adjustments throughout.
HIT16a: 554,183 lines: Based on files that Iouli Gordon sent me on June 27, 2017, (02_hit16_first-9iso) and June 30, 2017, (hit838corr). Fixed 19 lines with ABHW=0 and one line with intensity=0 (copied intensity from HIT12).
HIT16b: 559,874 lines: Downloaded from the HITRAN-online website on Nov 28, 2017 (5a1de32a.par). Includes isotopologs 11 & 12. Fixed same 19 lines with ABHW=0.
Every line of HIT16b is different from HIT16a. Mainly due to writing SBHW in ‘f5.3’ format instead of ‘f5.4’. Widths that were ‘.0678’ in HIT16a became ‘0.068’ in HIT16b. Is 2 sig figs good enough? In another case, ‘.1039’ became ‘0.103’ !?
In HIT16b, some intensities written as ‘2.980E-30’ in HIT16a, are ‘2.980e-30’ in HIT16b.
HIT16b contains CO2 isotopologs 11 and 12 (A and B)

## Slide 7: Types of Spectra and their Pros & Cons
Spectra | Pros | Cons
Laboratory (KP & JPL) | Well known cell conditions (T,P, VMR) Extreme isotopic enrichments possible Little interference (H2O, solar) Self-broadening can be investigated | Dim Source (lamp) so narrow spectral coverage and poor SNR Narrow range of temperatures
MkIV Balloon Occultation | Bright Source (sun) allows broad coverage (650-4850 cm-1) + high SNR Wide range of T/P/VMR conditions measured within minutes by same FTS Solar & instrumental features removed Large path lengths (~400 km) | Non-uniform atmospheric path Unknown atmospheric conditions (inferred from spectra) Interferences from other gases with possibly poor specroscopy
MkIV Ground-based | Bright Source (sun) allows broad coverage (650-4850 cm-1) + high SNR Long paths (up to 200 km) Sensitive to air-broadened widths | Broad regions blacked out: - H2O (1350-1900; 3350-4000 cm-1) - CO2 (650-700; 2280-2390 cm-1) Solar features present
TCCON Ground-based | Bright Source (sun) allows broad coverage (4000-14800 cm-1) + high SNR Long paths (up to 200 km) Sensitive to air-broadened widths | Some regions blacked out: - H2O (7000-7200 cm-1) Solar features present
IMO, main drawback of using atmospheric spectra for spectroscopic purposes, is that you need good linelists for all gases with significant absorption, not just the gas of current interest.

## Slide 8: Laboratory Spectra
Used 147 lab spectra of CO2. 137 from Kitt Peak + 10 from JPL (Keeyoon Sung)
Vast majority of CO2 spectra measured at room temperature, so limited ability to check T-dependent parameters.
One spectrum measured at 235K, one at 268K, the rest all above 290K.
Pressures from 0.1 to 700 Torr.
26 spectra are enriched in 13C, mainly covering the strong v3 band centered at 2330 cm-1.
Collective spectral coverage from 600 to 12,000 cm-1, although individual spectra are much narrower. Did not bother fitting beyond 7000 cm-1. No interest to TCCON or NDACC.
Of the 5733 theoretical spectra fits (39 windows x 147 spectra), only 1885 (30.8 %) could actually be performed due to the limited spectral coverage of the lab spectra.

## Slide 9: Properties of the 39 windows fitted
Center Width Gases fitted <Iso> Smax Stot <S> <E”>
693.50 49.40 co2 h2o 1.01 1.707E-19 2.929E-18 1.051E-19 335.3
754.50 65.50 co2 h2o 1.01 2.965E-21 4.756E-20 1.829E-21 998.8
827.20 68.60 co2 h2o 1.01 1.570E-23 2.546E-22 9.940E-24 1597.6
925.00 72.10 co2 h2o 1.03 2.147E-23 3.348E-22 1.336E-23 1686.9
980.00 42.10 co2 h2o nh3 1.01 2.244E-23 3.086E-22 1.605E-23 1586.3
1056.40 93.80 co2 h2o 1.02 3.461E-23 9.952E-22 2.225E-23 1553.0
1239.50 40.60 co2 h2o 3.05 5.651E-25 1.801E-23 3.594E-25 274.2
1280.60 39.80 co2 h2o ch4 3.07 5.996E-25 1.806E-23 4.081E-25 216.9
1367.40 51.80 co2 h2o ch4 3.07 6.561E-25 3.536E-23 4.497E-25 196.2
1857.40 16.50 co2 h2o 1.13 5.761E-25 6.328E-24 4.282E-25 1101.4
1906.50 71.00 co2 h2o 1.02 2.789E-23 6.322E-22 1.539E-23 359.6
1958.00 28.60 co2 h2o 1.01 3.045E-24 3.545E-23 2.205E-24 595.2
1982.50 17.00 co2 h2o 1.13 9.520E-25 5.430E-24 4.171E-25 1196.4
2082.00 178.00 co2 h2o co n2o 1.02 2.017E-22 6.184E-21 1.062E-22 378.0
2299.00 202.00 co2 h2o n2o co ch4 1.02 3.542E-18 1.012E-16 2.294E-18 261.1
2432.00 67.00 co2 n2o ch4 1.03 2.499E-24 6.402E-23 1.798E-24 1469.9
2502.00 70.00 co2 n2o hdo ch4 2.95 2.547E-25 1.508E-23 1.653E-25 304.7
2601.00 96.00 co2 n2o hdo ch4 3.05 4.210E-25 2.491E-23 2.698E-25 250.8
2760.00 62.00 co2 h2o hdo n2o ch4 3.05 6.336E-26 3.579E-24 4.224E-26 213.7
3155.00 42.00 co2 h2o n2o ch4 1.03 3.090E-25 5.115E-24 1.895E-25 530.9
3207.00 50.00 co2 h2o n2o 1.00 5.059E-25 7.592E-24 3.531E-25 419.7
3309.00 49.00 co2 h2o n2o 1.05 1.711E-24 2.793E-23 1.016E-24 580.3
3364.00 52.00 co2 h2o n2o 1.00 4.951E-24 8.645E-23 3.016E-24 422.2
3553.85 52.50 co2 h2o n2o 1.13 8.918E-21 8.408E-20 2.729E-21 817.1
3623.40 87.40 co2 h2o 1.03 3.887E-20 1.051E-18 2.633E-20 225.3
3713.50 83.00 co2 h2o n2o 1.01 5.925E-20 1.653E-18 3.892E-20 255.7
3811.00 74.00 co2 h2o n2o 1.03 2.364E-24 6.154E-23 1.635E-24 1480.5
3872.00 32.00 co2 h2o 1.87 3.783E-26 1.882E-24 2.300E-26 1318.1
3991.00 84.00 co2 h2o 1.22 2.389E-25 6.259E-24 1.136E-25 1024.5
4622.00 83.00 co2 n2o 2.81 2.753E-25 1.867E-23 1.619E-25 291.8
4812.00 184.00 co2 n2o 1.07 2.730E-22 8.300E-21 1.660E-22 282.8
4962.00 116.00 co2 n2o 1.01 1.319E-21 3.708E-20 8.561E-22 260.4
5096.00 152.00 co2 h2o n2o nh3 1.01 4.289E-22 1.216E-20 2.747E-22 271.2
6072.00 98.00 co2 1.07 1.731E-24 5.074E-23 1.090E-24 262.2
6211.00 128.00 co2 1.02 1.750E-23 5.000E-22 1.119E-23 268.0
6338.00 124.00 co2 1.00 1.779E-23 4.949E-22 1.153E-23 261.6
6506.00 124.00 co2 1.00 1.937E-24 5.793E-23 1.167E-24 282.7
6769.00 82.00 co2 h2o 2.01 6.380E-25 1.762E-23 4.267E-25 242.5
6940.00 120.00 co2 h2o 1.01 6.025E-23 1.703E-21 3.939E-23 259.5

## Slide 10: Properties of the windows fitted
Center: Center wavenumber of window (cm-1)
Width: Width of window (cm-1)
Gases fitted: Gases whose vmr is adjusted.
<Iso>: Intensity-averaged isotope number
Smax : Maximum individual line intensity
Stot : Total intensity of all lines
<S> : Intensity-averaged intensity.
<E”> : Intensity-averaged E”.
These properties are all independent of the fitted spectra.
The windows at 1239, 1280, 1327, 2502, 2601, 2760 all have <Iso> values close to 3, since the absorption is predominantly by the 628 isotopolog, the symmetric isotopologs (616, 636) being dark in the symmetric stretch bands. The absorption in the 6769 cm-1 window has <Iso>=2.00 since it arises entirely from the 636 isotopolog.

## Slide 11: Broad Window Approach
Why do my windows cover most of the Mid- and SW-IR region, rather than just the NDACC or TCCON windows?
NDACC windows tend to be narrow ~1 cm-1. Usually when there's a spectroscopy problem (e.g. strength bias, positions error, widths too narrow) it affects all lines in a given sub-branch similarly. So why not fix all the affected lines together, rather than just the one line that is currently used by NDACC?
This broad-band approach also provides more definitive feedback to the spectroscopists. If you tell them that the CO2 line at 3315.123 cm-1 is in the wrong position, they will just shrug. Of course, I could fix the problem manually, but the next time that the spectroscopist generates a new linelist, the problem will very likely re-appear.
On the other hand, if you tell the spectroscopist that all the R-branch lines of a particular band of a particular isotoplog are shifted by xx cm-1, or yy% too strong, then that is something that they may investigate and may ultimately fix by changing the fundamental spectroscopic constants. And this will likely have beneficial knock-on effects in other bands.
Finally, I hope that NDACC will start using wider windows. Fixing the spectroscopy only in the existing windows is self-defeating since poor spectroscopy outside is then cited as a reason why the window cannot be expanded.

## Slide 12: % RMS fits to laboratory spectra
# fcen width Nrow Npp hit08 hit12 atm16 hit16a hit16b
1 693.50 24.70 45 147 0.7415 0.6390 0.6390 0.6270 0.6270
2 754.50 32.75 45 147 0.5756 0.5648 0.5648 0.5640 0.5641
3 828.35 33.15 65 147 0.8154 0.8015 0.8015 0.8012 0.8012
4 925.00 36.05 67 147 0.4305 0.4303 0.4303 0.4299 0.4299
5 980.00 21.05 69 147 0.3186 0.3185 0.3185 0.3183 0.3183
6 1056.40 46.90 69 147 0.4018 0.4001 0.4001 0.3995 0.3995
7 1239.50 20.30 69 147 0.5242 0.5212 0.5212 0.5129 0.5128
8 1280.60 19.90 69 147 0.8698 0.8699 0.8699 0.8667 0.8666
9 1367.40 25.90 69 147 0.7754 0.7753 0.7753 0.7746 0.7746
10 1857.40 8.25 40 147 0.1698 0.1701 0.1701 0.1576 0.1576
11 1906.50 35.50 40 147 0.2291 0.2286 0.2286 0.2262 0.2262
12 1958.00 14.30 40 147 0.1783 0.1790 0.1790 0.1740 0.1740
13 1982.50 8.50 40 147 0.1387 0.1358 0.1358 0.1298 0.1298
14 2082.00 89.00 40 147 0.2560 0.2501 0.2501 0.2453 0.2453
15 2299.00 101.00 41 147 0.7384 0.6764 0.6751 0.6220 0.6109
16 2432.00 33.50 43 147 0.1350 0.1350 0.1350 0.1336 0.1337
17 2502.00 35.00 43 147 0.1195 0.1195 0.1195 0.1182 0.1182
18 2601.00 48.00 43 147 0.1222 0.1224 0.1224 0.1206 0.1195
19 2760.00 31.00 51 147 0.2624 0.2665 0.2665 0.2654 0.2658
20 3155.00 21.00 42 147 0.2981 0.2981 0.2981 0.2980 0.2980
21 3207.00 25.00 42 147 0.2716 0.2713 0.2713 0.2709 0.2709
22 3309.00 24.50 42 147 0.2442 0.2445 0.2439 0.2427 0.2427
23 3364.00 26.00 42 147 0.2695 0.2715 0.2684 0.2580 0.2580
24 3553.85 26.25 42 147 1.4921 1.0538 1.0090 0.9728 0.9673
25 3623.40 43.70 42 147 1.3930 1.1350 1.1174 0.9790 0.9787
26 3713.50 41.50 42 147 0.8171 0.6696 0.6696 0.6647 0.6658
27 3811.00 37.00 42 147 0.4608 0.4596 0.4596 0.4596 0.4596
28 3872.00 16.00 43 147 0.4270 0.4245 0.4245 0.4245 0.4245
29 3991.00 42.00 43 147 0.1692 0.1681 0.1681 0.1680 0.1680
30 4622.00 41.50 43 147 0.1576 0.1520 0.1520 0.1528 0.1527
31 4812.00 92.00 37 147 0.1816 0.1826 0.1804 0.1892 0.1893
32 4962.00 58.00 37 147 0.2923 0.2848 0.2823 0.2832 0.2836
33 5096.00 76.00 37 147 0.2139 0.2152 0.2143 0.2121 0.2123
34 6072.00 49.00 36 147 0.0992 0.0996 0.0988 0.0994 0.0994
35 6211.00 64.00 35 147 0.1301 0.1287 0.1235 0.1279 0.1280
36 6338.00 62.00 36 147 0.1372 0.1357 0.1296 0.1350 0.1352
37 6506.00 62.00 31 147 0.1277 0.1279 0.1277 0.1280 0.1280
38 6769.00 41.00 32 147 0.1818 0.1824 0.1824 0.1820 0.1821
39 6940.00 60.00 32 147 0.2814 0.2817 0.2817 0.2831 0.2832
Average over all windows: 0.3961 0.3690 0.3668 0.3594 0.3590

## Slide 13: RMS Fits to lab spectra
Plots shows the RMS spectral fit averaged over 147 lab spectra.
Upper panel shows absolute value of mean rms fit. Lower panel shows differences from HIT12.
Absolute value of RMS fit not important – this is generally dominated by instrumental issues (noise, channeling) and interfering absorption (e.g. H2O).
The variation of RMS from linelist to linelist shows the effect of the CO2 spectroscopy changes, since everything else is the same.
Big improvements for HIT16a,b in the 2300 and 3600 cm-1 regions.
Slightly worse than all other linelists in 4812 cm-1 window. Worse than ATM16 at 6000-6500 cm-1.
HIT16a and b produce very similar results which are hard to distinguish in this plot.

## Slide 14: One step backwards: frequency errors in HIT16
Upper Left: Pair of 18OCO lines at 4603.51 and 4603.62 cm-1 have incorrect positions in HIT16 linelist. These lines are the transitions:
0 1 1 21 0 1 1 01 P 14f
0 1 1 21 0 1 1 01 P 14e
Upper Right: Positions were correct in HIT12.
Lower-Left: Reverted positions to HIT12 values, keeping the HIT16 strengths and widths.
Several other line pairs of this transition have similar position problems in this band.

## Slide 15: What went wrong in 4812 cm-1 window ?
In terms of RMS spectral fits, in this window HIT16 is worse than all previous linelists (at least back to 2008). This is the spectral region used by OCO-2 for CO2 retrievals.
There appear to be two main problems:
Intensities of the “4 0 0 02 0 1 1 01” band of the 626 isotopolog are 10-15% too strong
Positions of the “2 0 0 12 0 0 0 01” and “2 0 0 13 0 0 0 01” bands of the 636 isotopolog are incorrect, at least with respect to the other bands in this window (which include N2O centered at 4731 cm-1, added for frequency calibration purposes)
In both cases, reverting the offending HIT16 parameters back to HIT12 improved the fits.
The next few slides illustrate these problems

## Slide 16: Example of position error in HIT16
Top: 5co2 lines (green) in 2380-2525 cm-1 interval are all left-shifted by 0.0085 cm-1.
Problem also present in 2500 cm-1 region (not shown). HIT12 positions were even worse.
Lower-Left: After left-shifting lines, peak residuals are 10x smaller and RMS residuals 5x smaller.

## Slide 17: Example of intensity error in HIT16
Upper Left: Fits to a KP lab spectrum in the 4800 cm-1 region used by OCO-2. Upward residuals arise from the “4 0 0 02 0 1 1 01” band of the 626 isotopolog.
Upper Right: zooms into four large residuals
Lower-Right: Reverted intensities and positions of 122 lines to HIT12 values, whose intensities are 10-15% smaller. Kept the HIT16 widths.
Other problems remain with this band.

## Slide 18: Retrieved CO2 VMR Scale Factors (lab)
700-1200 cm-1: Previous low bias of ~5% in CO2, has been improved with HIT16.
1200-1300 cm-1 : Previous high bias of 9% (628) has been removed with HIT16.
1800-1920 cm-1: HIT16 biased ~5% high. Previously no bias.
2400-2650 cm-1: HIT16 biased 3-4% high. Previously no bias.
TCCON windows at 6220 & 6338 cm-1 have a 1.4% bias using HIT16. Previously much smaller.
TCCON
CO2 bands

## Slide 19: Retrieved CO2 VMR Scale Factors (lab)
HIT08 39 0.9866 0.00792
HIT12 39 0.9925 0.00838
ATM16 39 0.9850 0.00805
HIT16a 39 1.0207 0.00801
HIT16b 39 1.0206 0.00802
Weighted mean values of the VMR scale factors over all 39 fitted windows, together with their standard errors.
The HITRAN 2016 linelist produces CO2 values that are 3% larger on average than previous linelists.
HIT08 has the smallest standard error (i.e. best consistency), and HIT12 the largest.

## Slide 20: Lab Spectra: Summary & Conclusions
RMS Fits:
HIT08 is clearly the worst overall, although in 4/39 windows it still remains the best of the five linelists.
Comparing HIT12 and ATM16. They produce similar results, but in general ATM16 is better. Which it should be because it is largely based on HIT12, except in regions where other linelists (e.g. Toth 2008) were found to be better. And on top of this, ad hoc empirical adjustements have further improved ATM16.
Comparing ATM16 with HIT16, the latter is generally better.
Comparing HIT16a and HIT16b. They produce very similar results. The latter is better in the 2300 cm-1 region in 13C-enriched spectra due to the addition of isotopologs 11 & 12.
Retrieved CO2 amounts:
HIT16 mostly fixes previous dip below 1200 cm-1
HIT16 is biased high over most windows in the 1900-2700 cm-1 region, worse than previous linelists.
Overall consistency of retrieved CO2 amounts was worst in HITRAN12

## Slide 21: Effect of Line Mixing (LM)
# Fcen Width Nrow Npp hit08 hit12 atm16 hit16a hit16b
36 6338.00 62.00 36 147 0.1372 0.1357 0.1296 0.1350 0.1352
36LM 6338.00 62.00 36 147 0.1370 0.1348 0.1288 0.1340 0.1342
37 6506.00 62.00 31 147 0.1277 0.1279 0.1277 0.1280 0.1280
37LM 6506.00 62.00 31 147 0.1276 0.1270 0.1270 0.1270 0.1271
In general LM wasn’t performed due to speed considerations (would have to use compute_lm_absco). As a test, two windows (6211 and 6338 cm-1) were fitted with and without line mixing. LM improved RMS fits for all linelists. For the ATM linelist the improvement was less than for the HITxx linelists, hinting that the empirical adjustments had partly compensated for unmodelled LM effects. But in these two windows the ATM16 fits without LM were still better than any of the HITxx linelists with LM, implying that the ATM16 linelist embodies some genuine spectroscopic improvements.

## Slide 22: MkIV Balloon spectra
An occultation of MkIV balloon spectra was fitted, covering altitudes from 9 to 37 km, temperatures from 210K to 250K, and pressures from 3 mbar to 300 mbar. These spectra were all acquired in ~30 minutes during which instrument remained stable.
The MkIV instrument covers the 650 to 5650 cm-1 region at 0.01 cm-1 spectral resolution (60 cm OPD) using two detectors in parallel (HgCdTe 650-1850; InSb 1850-5650 cm-1).
Only 33 of the 39 lab windows covered by the lab spectra, could be fitted using MkIV balloon spectra. But in these 33 windows, 100% coverage is achieved (i.e., every MkIV spectrum covers every window).
This high degree of coverage makes the MkIV spectra especially good at evaluating band-to-band biases. The 694 cm-1 CO2 band is measured simultaneously in the same airmass as the 5096 cm-1 CO2 band in all spectra. In the lab, these are never measured simultaneously.
Balloon spectra are sensitive to line positions and the T-dependence of intensities.

## Slide 23: Properties of the 33 balloon windows
Center Width Gases fitted <Iso> Smax Stot <S> <E”>
694.6 47.2 co2 h2o o3 1.01 1.714E-19 2.572E-18 1.148E-19 288.7
754.5 65.5 co2 h2o o3 1.01 2.998E-21 4.812E-20 1.849E-21 999.2
827.2 68.6 co2 h2o o3 hno3 ccl3f chclf2 1.01 1.582E-23 2.565E-22 1.002E-23 1598.0
925.0 72.1 co2 h2o hno3 ccl2f2 sf6 1.03 2.230E-23 3.478E-22 1.386E-23 1688.1
980.0 42.1 co2 h2o o3 1.01 2.346E-23 3.226E-22 1.679E-23 1586.6
1056.4 93.8 co2 h2o o3 ccl2f2 ccl3f 1.02 3.583E-23 1.031E-21 2.304E-23 1553.8
1239.5 40.6 co2 h2o ch4 n2o 3.05 5.700E-25 1.812E-23 3.628E-25 274.0
1280.6 39.8 co2 h2o ch4 n2o hno3 clno3 3.06 6.092E-25 1.834E-23 4.148E-25 216.8
1367.4 51.8 co2 h2o ch4 hno3 hdo 3.07 6.683E-25 3.578E-23 4.567E-25 195.5
1857.9 15.3 co2 h2o o3 no n2o 1.15 6.255E-25 6.503E-24 4.733E-25 1077.4
1906.5 71.0 co2 h2o n2o no o3 cof2 1.02 2.904E-23 6.648E-22 1.602E-23 357.0
1958.0 28.6 co2 h2o cof2 1.01 2.937E-24 3.431E-23 2.120E-24 601.0
1982.5 17.0 co2 h2o o3 1.15 9.446E-25 5.389E-24 4.140E-25 1193.8
2082.5 177.0 co2 h2o o3 co n2o ocs 1.02 2.022E-22 6.195E-21 1.066E-22 377.3
2299.3 250.3 co2 h2o o3 n2o co ch4 1.02 3.543E-18 1.012E-16 2.293E-18 261.1
2430.6 64.2 co2 n2o ch4 1.03 2.634E-24 6.758E-23 1.910E-24 1468.8
2501.9 69.6 co2 n2o ch4 2.95 2.538E-25 1.509E-23 1.643E-25 307.5
2601.0 96.0 co2 n2o hdo ch4 3.05 4.222E-25 2.501E-23 2.701E-25 251.4
2760.0 62.0 co2 h2o o3 n2o ch4 hcl 3.06 6.618E-26 3.782E-24 4.358E-26 213.7
3155.0 38.0 co2 h2o o3 n2o ch4 1.03 3.098E-25 5.111E-24 1.908E-25 531.4
3206.7 40.5 co2 h2o o3 n2o ch4 1.00 5.108E-25 7.411E-24 3.682E-25 402.7
3309.0 49.0 co2 h2o n2o hcn 1.05 1.714E-24 2.797E-23 1.018E-24 578.5
3364.0 52.0 co2 h2o n2o hcn 1.00 4.910E-24 8.588E-23 2.984E-24 425.7
3553.8 52.4 co2 h2o n2o hno3 1.13 8.843E-21 8.309E-20 2.711E-21 816.5
3623.4 87.4 co2 h2o 1.03 3.835E-20 1.039E-18 2.601E-20 224.9
3713.5 83.1 co2 h2o o3 n2o hf hdo 1.01 5.851E-20 1.632E-18 3.846E-20 255.3
3811.2 74.0 co2 h2o o3 n2o ch4 hf hdo 1.03 2.299E-24 5.982E-23 1.589E-24 1480.3
3871.9 31.6 co2 h2o o3 n2o ch4 hf hdo 1.88 3.703E-26 1.849E-24 2.266E-26 1311.3
3991.0 84.0 co2 h2o o3 ch4 hf 1.21 2.508E-25 6.537E-24 1.205E-25 1029.2
4622.1 82.8 co2 h2o o3 n2o ch4 2.81 2.715E-25 1.836E-23 1.600E-25 290.1
4812.0 184.0 co2 h2o n2o ch4 1.07 2.732E-22 8.308E-21 1.662E-22 283.3
4962.0 116.0 co2 h2o o3 n2o 1.01 1.287E-21 3.635E-20 8.344E-22 262.5
5096.0 152.0 co2 h2o n2o 1.01 4.210E-22 1.196E-20 2.698E-22 271.8
There are small differences between the balloon windows and the first 33 of the lab windows.
Changes were made to avoid interferences in the balloon spectra that caused large residuals.

## Slide 24: % RMS residuals fitting MkIV balloon spectra:
Iwin fcen width Npp hit08 hit12 atm16 hit16a hit16b
1 694.60 23.60 38 0.6793 0.6590 0.6590 0.6544 0.6544
2 754.50 32.75 38 0.8280 0.7699 0.7699 0.7661 0.7661
3 827.20 34.30 38 0.3490 0.3417 0.3417 0.3416 0.3416
4 925.00 36.05 38 0.2932 0.2928 0.2928 0.2927 0.2927
5 980.00 21.05 38 0.4609 0.4601 0.4601 0.4599 0.4599
6 1056.40 46.90 38 0.4219 0.4225 0.4225 0.4218 0.4218
7 1239.50 20.30 38 0.2532 0.2528 0.2528 0.2530 0.2530
8 1280.60 19.90 38 0.4317 0.4314 0.4314 0.4314 0.4314
9 1367.40 25.90 38 1.1336 1.1337 1.1337 1.1335 1.1335
10 1857.90 7.65 38 0.5770 0.5771 0.5771 0.5757 0.5757
11 1906.50 35.50 38 0.7009 0.7026 0.7026 0.7036 0.7036
12 1958.00 14.30 38 0.5468 0.5450 0.5450 0.5498 0.5498
13 1982.50 8.50 38 0.4958 0.4884 0.4884 0.4879 0.4879
14 2082.50 88.50 38 0.7596 0.7534 0.7531 0.7523 0.7523
15 2299.30 125.15 38 0.5404 0.5184 0.5184 0.4852 0.4852
16 2430.60 32.10 38 0.1819 0.1844 0.1844 0.1806 0.1806
17 2501.90 34.80 38 0.2067 0.2062 0.2062 0.2065 0.2065
18 2601.00 48.00 38 0.2565 0.2559 0.2559 0.2560 0.2560
19 2760.00 31.00 38 0.2644 0.2634 0.2634 0.2632 0.2632
20 3155.00 19.00 38 0.5258 0.5252 0.5252 0.5245 0.5245
21 3206.75 20.25 38 0.2198 0.2173 0.2173 0.2144 0.2144
22 3309.00 24.50 38 0.2037 0.1913 0.1801 0.1877 0.1877
23 3364.00 26.00 38 0.2434 0.2194 0.2122 0.2109 0.2109
24 3553.80 26.20 38 1.4797 0.8086 0.7476 0.7088 0.7088
25 3623.40 43.70 38 1.3081 0.8339 0.8263 0.7685 0.7685
26 3713.50 41.55 38 0.6184 0.5095 0.5095 0.4919 0.4919
27 3811.20 37.00 38 0.9419 0.9058 0.9058 0.9054 0.9054
28 3871.90 15.80 38 1.1206 1.0633 1.0633 1.0633 1.0633
29 3991.00 42.00 38 0.4543 0.4539 0.4539 0.4539 0.4539
4622.10 41.40 38 0.2909 0.2797 0.2797 0.2793 0.2793
4812.00 92.00 38 0.4907 0.4934 0.4910 0.5335 0.5335
4962.00 58.00 38 0.5920 0.5727 0.5704 0.5708 0.5708
5096.00 76.00 38 0.5279 0.5287 0.5274 0.5217 0.5217
Average over all windows 0.5575 0.5110 0.5084 0.5045 0.5045

## Slide 25: RMS fitting residuals (MkIV balloon)
Plots shows the RMS spectral fit averaged over 38 balloon spectra covering a wide range of P/T conditions.
Upper panel shows absolute value of mean rms fit. Lower panel shows differences from HIT12 values.
Absolute RMS values are unimportant; these are generally dominated by instrumental issues (noise, channeling) and interfering absorption (e.g. H2O).
The variation of RMS from linelist to linelist shows the effect of the CO2 spectroscopy changes, since everything else is the same.
HIT16a & HIT16b are indistinguishable.
Big improvements seen for HIT16a,b linelists in 2300 and 3600 cm-1 regions. But worse than all other linelists in the 4812 cm-1 window.

## Slide 26: CO2 VMR Scale factors (MkIV balloon)
HIT16a and HIT16b linelists produce results that are indistinguishable.
Below 1950 cm-1, HIT16a,b linelists produce larger retrieved CO2 amounts than other linelists.

## Slide 27: Summary of Balloon Results
RMS Spectral Fits:
No difference whatsoever in retrievals or fits using HIT16a and HIT16b linelists, confirming that differences seen in lab spectra were predominantly due to small SBHW changes. Self-broadening of CO2 is always negligible for atmospheric spectra.
Big improvements seen for HIT16a,b linelists in 2300 and 3600 cm-1 regions. But worse than all other linelists in 4812 cm-1 window, due to 13CO2 line position & intensity errors:
‘2 0 0 12 0 0 0 01’ band of 13CO2
‘4 0 0 02 0 1 1 01’ 12CO2 hot band
‘2 0 0 13 0 0 0 01’ band of 13CO2
‘1 0 0 12 1 0 0 02’ v3 band of 13CO2
‘3 0 0 01 1 1 1 02’
Retrieved CO2 Amounts:
No dip in retrieved CO2 (VSF) at low wavenumbers.
Below 1950 cm-1, HIT16a,b linelists produce larger retrieved CO2 amounts than other linelists.

## Slide 28: MkIV Ground-based spectra
A representative subset of 125 MkIV ground-based spectra was fitted. These cover the 1986-2014 period from a variety of sites, with a wide range of solar zenith angles (13 to 89 deg), surface temperatures (-33 to +35C), relative humidities (9 to 86%), and pressures (640 to 1025 mbar). These spectra were pre-selected for high quality and for low H2O amounts, so that CO2 bands with H2O interference can be evaluated.
Maximum OPDs are either 57, 65, or 117 cm.
The MkIV instrument currently covers the 650 to 5650 cm-1 region simultaneously using two detectors in parallel (HgCdTe 650-1850; InSb 1850-5650 cm-1). All spectra are fitted in each window. Only 32 of the 39 windows covered by the lab spectra, could be fitted using MkIV spectra. A total of 32 x 125 = 4000 spectral fits were performed.
Ground-based spectra are sensitive to the assumed line shapes (ABHW, Pshift) and their T-dependences.

## Slide 29: RMS Spectral fits (MkIV Ground)
iwin fcen half-wid Nrow Npp hit08 hit12 atm16 hit16a hit16b
1 755.20 32.05 125 125 1.1056 1.0807 1.0807 1.0891 1.0891
2 827.20 34.30 125 125 0.5846 0.5832 0.5832 0.5812 0.5812
3 925.00 36.05 125 125 0.3430 0.3446 0.3446 0.3445 0.3445
4 980.00 21.05 125 125 0.4403 0.4435 0.4435 0.4428 0.4428
5 1056.40 46.90 125 125 0.6606 0.6573 0.6573 0.6570 0.6570
6 1239.50 20.30 125 125 0.7682 0.7684 0.7684 0.7684 0.7684
7 1280.60 19.90 125 125 0.2374 0.2373 0.2373 0.2374 0.2374
8 1367.40 25.90 125 125 0.1009 0.1012 0.1012 0.1009 0.1009
9 1857.90 7.65 125 125 0.2444 0.2442 0.2442 0.2444 0.2444
10 1910.30 29.70 125 125 0.5811 0.5822 0.5822 0.5796 0.5796
11 1960.45 11.85 125 125 0.6311 0.6307 0.6307 0.6346 0.6346
12 1982.50 8.50 125 125 0.6969 0.6963 0.6963 0.6962 0.6962
13 2082.50 88.50 125 125 1.1643 1.1738 1.1739 1.1747 1.1747
14 2299.30 125.15 125 125 0.3992 0.3980 0.3980 0.3978 0.3978
15 2430.60 32.10 125 125 0.2377 0.2353 0.2353 0.2382 0.2382
16 2501.90 34.80 125 125 0.2552 0.2549 0.2549 0.2549 0.2549
17 2605.00 42.00 125 125 0.3747 0.3747 0.3747 0.3747 0.3747
18 2760.00 31.00 125 125 0.4243 0.4239 0.4239 0.4238 0.4238
19 3159.00 15.20 125 125 1.2763 1.2758 1.2758 1.2758 1.2758
20 3206.75 18.50 125 125 0.8082 0.8077 0.8077 0.8076 0.8076
21 3309.00 22.50 125 125 0.4745 0.4742 0.4742 0.4739 0.4739
22 3360.50 22.00 125 125 0.5360 0.5387 0.5384 0.5357 0.5357
23 3553.80 26.20 125 125 0.1913 0.1928 0.1928 0.1929 0.1929
24 3623.40 43.70 125 125 0.1345 0.1376 0.1376 0.1383 0.1383
25 3713.50 41.55 125 125 0.0149 0.0147 0.0147 0.0148 0.0148
26 3811.20 37.00 125 125 0.0238 0.0238 0.0238 0.0239 0.0239
27 3871.90 15.80 125 125 0.1410 0.1410 0.1410 0.1410 0.1410
28 3991.00 42.00 125 125 0.7954 0.7925 0.7925 0.7928 0.7928
29 4627.00 34.40 125 125 0.3749 0.3726 0.3726 0.3728 0.3728
30 4812.35 91.65 125 125 0.7805 0.7828 0.7823 0.7804 0.7804
31 4962.00 58.00 125 125 0.8659 0.8352 0.8351 0.7891 0.7891
32 5094.75 73.25 125 125 0.8318 0.8277 0.8277 0.8261 0.8261
Average over all windows 0.5156 0.5140 0.5140 0.5127 0.5127

## Slide 30: % RMS from ground-based MkIV
Plots shows the RMS spectral fit averaged over 125 spectra covering a wide range of P/T conditions.
Upper panel: absolute value of mean rms fit. Lower panel: differences from HIT12 values.
Absolute RMS values are not important; these are generally dominated by instrumental issues & interfering absorption (e.g. H2O).
The variation of RMS from linelist to linelist shows the effect of the CO2 spectroscopy changes, since everything else is the same.
HIT16a &b are indistinguishable.
Large residuals at 3155 cm-1 due to neglect of LM in interfering CH4.
Small residuals at 1350 cm-1 and 3700-3900 cm-1 due to windows being blacked out by H2O.
Big improvement seen for HIT16a,b linelists at 4960 cm-1 .
HIT08 still best in several windows (e.g. 2080 cm-1).

## Slide 31: VSFs from ground-based MkIV
Retrieved CO2 amounts, expressed as a ratio to the mean of all windows.
The variation from linelist to linelist shows the effect of the CO2 spectroscopy changes, since everything else is the same.
HIT16a & HIT16b results are indistinguishable.
Big improvements seen for HIT16a,b linelists at 4960 cm-1 .
HIT08 still best in several windows.

## Slide 32: Ground-based TCCON spectra
25 spectra from various TCCON sites covering 4000 to 15000 cm-1 at 0.020 cm-1 resolution (45 cm Max OPD).
CO2 doppler full-widths in the region are 0.010 at 4800 cm-1 and 0.014 cm-1 at 6300 cm-1, so not much would be gained by a higher Max OPD
10 windows could be fitted.

## Slide 33: % RMS from ground-based TCCON
iwin fcen Width Nrow Npp hit08 hit12 atm16 hit16 hit16b
1 4627.00 34.40 25 25 0.2615 0.2577 0.2577 0.2581 0.2581
2 4812.35 91.65 25 25 0.4379 0.4334 0.4323 0.4249 0.4249
3 4962.00 58.00 25 25 0.6784 0.6374 0.6370 0.5771 0.5771
4 5094.75 73.25 25 25 0.7108 0.7059 0.7058 0.7012 0.7012
5 6071.70 48.70 25 25 0.2279 0.2307 0.2285 0.2268 0.2268
6 6211.00 64.00 25 25 0.2051 0.2026 0.1942 0.2023 0.2023
7 6338.00 60.55 25 25 0.2012 0.1993 0.1909 0.1992 0.1992
8 6506.25 60.75 25 25 0.1780 0.1802 0.1780 0.1804 0.1804
9 6769.00 41.10 25 25 0.8414 0.8416 0.8416 0.8415 0.8415
10 6937.50 59.50 25 25 0.6705 0.6734 0.6734 0.6716 0.6716
Average over all windows 0.4413 0.4362 0.4339 0.4283 0.4283

## Slide 34: % RMS from ground-based TCCON

## Slide 35: VSF from ground-based TCCON
HITRAN16a,b linelists are indistinguishable.
Lower CO2 amounts are generally retrieved with HIT16 linelists generally (except at 6040 cm-1).
The 6220 and 6340 cm-1 (TCCON) windows produce similar results with all pre-HIT16 linelists, but the HIT16 linelists introduce a 2% discrepancy between the 6220 and 6340 cm-1 windows.

## Slide 36: Conclusions – RMS fits
The HITRAN 2016 linelist represent embodies some major improvements over previous linelists, even without the two new isotopologs (A & B).
In all categories (lab, balloon, ground) of spectral measuements, the HIT16 linelists gives the best overall RMS fits. HIT08 linelist gives the worst overall fits. HITRAN12 and ATM16 are intermediate.
That said, there were certain combinations of spectral measurements/windows where HIT16 was not the best.
In the 4812 cm-1 window, HIT16 gave the poorest fits of all linelists to lab and balloon spectra, which are sensitive to line positions. In the same window, HIT16 gave the best fits to ground-based MkIV and TCCON spectra, which are strongly pressure-broadened.
Above 6100 cm-1, the HIT16 linelist is never the best. In the two TCCON CO2 bands at 6220 and 6340 cm-1, the ATM16 linelist gives the best RMS fits.
In fits to ground-based MkIV spectra in the 2080 cm-1 window, HIT08 gave the best fits and HIT16 the worst. This was not the case in fits to lab or balloon spectra, implying that the HIT16 positions are good and that the widths/shifts are inadequate.

## Slide 37: Conclusions – Retrieved CO2 amounts
The HIT16b SBHW field no longer has enough significant digits. The current f5.3 format imposes a digitization error of up to 1%. This has no impact on atmospheric spectra, or air-broadened lab spectra. But for modest pressure pure CO2 lab samples, this causes a detectable degradation of the spectral fits.
The low wavenumber dip in CO2 amounts (VSF) retrieved from lab spectra is not seen in MkIV atmospheric spectra (ground or balloon). Either the low-wavenumber lab measurements over-estimated the amount of CO2 in their cell. Or MkIV low-wavenumber measurements have a systematic error, not present at higher wavenumbers and not evident in retrievals of other gases.
A worsening of the rms residuals in HIT16, relative to HIT12 and atm16, is seen around the 13CO2 band (2 0 0 12 - 0 0 0 01) centered at 4887 cm-1. This is due to a ~3% increase in the intensities of this band, and a ~1 mK shift in line positions, which don’t seem warranted. This isn’t evident from the retrieved CO2 amounts (from all isotopes) because this is dictated by the much-stronger 12CO2 lines.

## Slide 38: Implications for TCCON/NDACC
The HITRAN 2016 CO2 linelist is a non-starter for TCCON. The CO2 bands at 6211 and 6338 cm-1, which are consistent to 0.1% using the ATM16 linelist, have a bias of 1-2% using HIT16 with the 6211 cm-1 window giving the larger CO2 amounts in both lab and TCCON spectra.
Also, the RMS residuals for these two windows worsen using the HIT16 linelist, as compared with ATM16. This is also the case for the 6506 cm-1 window.
For the 4850 cm-1 region, used by OCO-2 and for attempted profile retrievals from TCCON, there are errors in line positions and intensities for several of the weaker bands (13CO2 and 12CO2 hot-bands) which drive up the residuals in low-pressure spectra (lab & balloon).The new widths, however, seem to be improved based on ground-based MkIV & TCCON fits.
Below 4800 cm-1, the HIT16 is generally superior to previous linelists and should be adopted by NDACC.
If the HITRAN16 widths & shifts were fixed in the 4850 cm-1 region, and then the result merged with the ATM16 linelist in the 6100-7000 cm-1 region, then this would represent the best that could be currently achieved.
HITRAN 2016 CO2 is “two steps forward”. With care we can avoid the “one step backward”.