## Slide 1
Temporal Variation of Greenhouse Gases observed by FTIR
at Hefei site, China
Changgong Shan, Wei Wang, Youwen Sun, Cheng Liu
Key Laboratory of Environmental Optics and Technology, AIOFM
cgshan@aiofm.ac.cn
Notes: My purpose today is to give a detaile of the FTIR observed at Hefei Site

## Slide 2
FTIR system of the Hefei site
Parameter setting
Observed results
EM27 results
CONTENTS

## Slide 3
01
FTIR system of the Hefei site

## Slide 4
01
FTIR system of the Hefei site
The Hefei site (31.91 N, 117.17 E, 29 m), adjacent to a lake in a flat terrain, is located in the north-western rural area of Hefei city in eastern China
Operated by Key Laboratory of Environmental Optics and Technology, Anhui Institute of Optics and Fine Mechanics

## Slide 5
The high-resolution FTIR instrument (Bruker IFS 125HR), and a solar tracker (A547N) on the roof of the lab building, to monitor the atmospheric trace gas profiles and total columns.
IFS125HR
01
FTIR system of the Hefei site
Clear sky day:
Alternating
NIR & MIR
Partly cloudy day:
Only NIR or MIR

## Slide 6
02
Parameter setting

## Slide 7
A minimum spectral range of 4000-9000 cm-1.
Maximum OPD >= 45 cm with phase resolution of at least 1 cm-1.
02
Parameter setting
TCCON request
Hefei Site
Spectral range covers 4000–11000 cm-1 using a CaF2 beam-splitter and an InGaAs detector.
Spectra are recorded at Max OPD = 45 cm. The spectra resolution is 0.02 cm-1.
Detector & Beam split

## Slide 8
FTS sun tracker pointing with an accuracy of 1 mrad (~0.05°, or 3 arcminutes) or better.
Tracker accuracy should be routinely monitored in one dimension using the solar-telluric shift (S-G shift).
02
Parameter setting
TCCON request
Hefei Site
sun tracker pointing with an accuracy of 0.01°
Tracker is pointing directly at the center of the sun.
Sun tracker
Notes: We also using the solar telluric shift that retrieved from O2 window to monitor the tracker accuracy.

## Slide 9
Surface pressure measurements accurate to 0.3 mbar or better.
Surface temperature measurements accurate to better than 1 K.
02
Parameter setting
TCCON request
Hefei Site
The ZENO weather station at Hefei uses a pressure sensor that has an accuracy of +/-0.2mbar.
The ZENO weather station at Hefei uses a HUMITTER 50U/50Y(X) Integrated Humidity and Temperature Transmitter which has a temperature accuracy of ± 0.1°C, and a humidity accuracy of ± 1%.
Weather parameter
Notes: I have checked the weather station logfile and found that the voltage of station battery have been with low voltage and could not be powered properly before 04/29/2020.

## Slide 10
The voltage of station battery have been with low voltage and could not be powered properly before 04/29/2020
The weather data were corrected by another weather station that nearby the site
pout-pmod is outside the 3 hPa limit in 2020.02-2020.05
02
Parameter setting
Weather parameter

## Slide 11
Laser sampling errors less than 0.00024 of the sample step.
The corresponding bias in XCO2 is estimated to be 0.02% or less.
02
Parameter setting
TCCON request
Hefei Site
The instrument uses a ECL03 laser sampling board. The ghost was minimized by adjusting the potentiometer on the board.
A M16 controller is used with the XPM parameter turned on to correct for ghosts while sampling.
Laser sampling errors
Notes: Additionally, the I2S code is also enabled for the LSE correction.

## Slide 12
02
Routine procedures for monitoring instrument line shape (ILS).
There is an HCl cell that is permanently placed in the path of the solar beam.
Monthly lamp measurements are recorded and processed using LINEFIT 14.5.
The ME is between 1.034 and 0.965, the ME varies less than 5%. and the phase errors are lower than 0.01 rad
Parameter setting
ILS retrieval results

## Slide 13
02
we corrected the timing error iteratively by adding or subtracting a step value until the diurnal variation of Xair was symmetric and less than 1%
Before the timing error correction is applied, the daily Xair varies more than 4% over a large range from 0.957 to 1.021.
After the correction, with a minus 47s in the retrieval, the daily Xair approaches on 0.983 and varies less than 1%
Parameter setting
Timing error correct
Notes: In order to correct timing error-related bias, we assumed a constant daily timing error and a linear drift from point that the time synchronisation failed until it was discovered.

## Slide 14
03
Observed results

## Slide 15
Precision: 1.07%
Annual increase:-3.81±0.88 ppb/yr
Seasonal amplitude:29.26±3.98 ppb
Observed results
03
Precision: 0.04%
Annual increase:2.64±0.13 ppm/yr
Seasonal amplitude:7.1±0.98 ppm
Precision: 0.16%
Annual increase:6.8±0.1 ppb/yr
Seasonal amplitude:35.75±4.97 ppb
XCO2
XCH4
XCO
Notes: GGG2020, standed TCCON window

## Slide 16
Precision: 0.04%
Annual increase:-6.90±1.07ppt/yr
Seasonal amplitude:18.9±3.43ppt
XHF
03
Precision: 0.04%
Annual increase: close to 0
Seasonal amplitude:7225.4±103.3ppm
XH2O
Precision: 0.20%
Annual increase:1.06±0.4 ppb/yr
Seasonal amplitude:4.64±0.99 ppb
XN2O
Observed results
Notes: 基于典型的晴朗天11：00到13：00两个小时内的观测数据，获得反演误差，并根据气体的测量值变化估算气体的观测精度。
With an sunny day select 11:00 to 13:00 two hours data, calculate the data standed deviation and mean value, the ratio of SD and mean value.

## Slide 17
03
CO2
Bias: -0.52 ±1.63ppm
R2 : 0.89
CH4
Bias: 1.60 ±13.0ppb
R2 : 0.77
CO2
Bias: 0.81±1.73ppm
R2 : 0.83
CH4
CO2
XCO2 and XCH4 comparison with GOSAT
XCO2 comparison with OCO-2
Observed results

## Slide 18
Surface concentration
Tropospheroc column
Total column
Δ CO2 /ΔCO ratio in Hefei has been increasing year by year, indicating that combustion efficiency is improving, which is related to the country's promotion of energy conservation and emission reduction;
Surface concentration, tropospheric, and total column ratio show a gradual upward trend, because the average value of the upper layer concentration will dilute the surface concentration results.
区域CO排放反演
03
Observed results
The enhancement ratio of CO2 /CO
Notes: Using co2 and CO data that observed in surface, troposphere and total column to calculate

## Slide 19
04
EM27 results

## Slide 20
EM27 results
04
EM-27
MAX-DOAS
31.17, 121.43
CO2
CH4
The ratio of NO2 to CO2 for air masses from land is significantly higher than that of air masses from sea
CO2 has a peak value in the morning, caused by the morning rush hour traffic;
Concentration of CH4
and CO2 both increased at noon, maybe caused by cooking in restaurants, canteens and communities at noon。
Airmass from Sea
 | Sea | Land
△NO2/△CO2 (ppb/ppm) | 0.11±0.05 | 0.58±0.04
Corr | 0.41 | 0.75
Airmass from land
Using NO2 as a tracer to determine the contribution of different motor vehicle emission sources to CO2 emissions in Shanghai.
Observe in Shanghai
Notes: A campaign was conducted for observations of trace gases with EM27/SUN and MAX-DOAS system at Shanghai from October 2020 to December 2020. Atmospheric CO2 and NO2 from the land sources show higher correlation, with higher ratio of NO2 to CO2 compared to that derived from the gases from the sea sources.

## Slide 21
∆XCH4： 41.09±4.64(ppb)
Compare with Hefei site
04
94.44E，29.46N，ALT 3326m
Linzhi Site
∆XCO2：2.68±1.08(ppm)
Compare with Hefei site
EM27 results
Notes: 41.09

## Slide 22
We Thank
David Grifﬁth，Voltaire Velazco，
Nick Deutscher, David Pollard and Frank Hase
for great assistance

## Slide 23
Thank You!
Hefei Institutes of Physical Science, Chinese Academy of Science
www.hf.cas.cn