## Slide 1
Roadmap for future GGG development
and
Application of machine learning to XCO2 diurnal cycles
Joshua L. Laughner1, Calla Marchetti1,2, Geoffrey C. Toon1, Debra Wunch3, and Paul Wennberg4,5
1 Jet Propulsion Laboratory, California Institute of Technology
2 University of California, Los Angeles
3 Department of Physics, University of Toronto
4 Department of Geological and Planetary Sciences, California Institute of Technology
5 Department of Engineering and Applied Science, California Institute of Technology

## Slide 2
GGG development roadmap

## Slide 3: GGG versioning nomenclature
GGG2020
GGG2020.1, GGG2020.2
GGG202X or GGGv3
Current stable algorithm version
Minor (post processing-only) updates
Major update to GFIT and/or I2S
Post processing-only updates done at:
  Caltech if change is straightforward to apply to the netCDF files, or
  Individual sites if additional data from other files needed - save your run directories!
Major updates planned to be run by individual sites

## Slide 4: GGG development overview
Upcoming milestones:
GEOS FP-IT to GEOS IT changeover
Xluft-based bias correction for XCO2
Temperature-based biased correction for XN2O and XCH4
CO2 & CO (TARDISS) and CH4 partial columns
Improved post-processing mechanics
Non-linearity correction in I2S
Modeling non-ideal ILS in GFIT
Improved spectroscopy for N2O, CH4, and CO2
Support for modern gfortran compilers
GGG2020
GGG2020.1
GGG2020.2
GGG202X

## Slide 5: GGG (notional) development timeline
GGG2020
GGG2020.1, GGG2020.2
GGG202X
June 2023
Oct 2023
GGG2020.1 bias corr. complete
Dec 2023
GGG2020.1 data release
Aug 2024
GGG2020.2 alg. complete
Dec 2024
GGG2020.2 data release
Mid- 2025
Partial column products release
Late 2025
GGG202X ready for beta testing
Change to XCO2
Can be generated at Caltech
Change to XCH4 and XN2O
New products
Jul 2023
GEOS IT support ready

## Slide 6: GEOS FP-IT to GEOS IT changeover (GGG2020)
GGG2020 uses GEOS FP-IT for the meteorology and as input for the VMR priors
Goddard plans to end FP-IT production ~end 2023, switching to the new GEOS IT product
GEOS IT has the same variables as FP-IT, but is an updated assimilation system
Three main tasks:
  Update CO priors to reflect changes in CO emissions between FP-IT and IT
  Modify the automatic priors generation to handle the FP-IT to IT switch
  Evaluate changes in Xgas products introduced by the new meteorology
There will be a hard changeover date after which the automatic priors will use GEOS IT data. We are coordinating this with OCO -2 and -3.
Priors before the changeover date will not be regenerated with GEOS IT except as needed for testing in task #3 above

## Slide 7: Xluft-based bias correction for XCO2 (GGG2020.1)
Comparison with in situ profiles identified a bias in XCO2 correlated with Xluft
  Grey line at right is only fit to data in 0.996 ≤ Xluft ≤ 1.002, but predicts the two Park Falls points at Xluft ≈ 0.988 well
  NB: Only Sodankylä has nonlinearity correction in this plot
This should be driven by factors such as misalignment, nonlinearity, and surface pressure errors
Still working to reproduce this behavior in tests with synthetically “bad” data

## Slide 8: Xluft-based bias correction for XCO2 (GGG2020.1)
This correction has become more urgent since a team working on machine learning-based filtering and bias correction for OCO-2 noticed time trends in OCO-2 vs. TCCON biases that correlate with Xluft (top)
We are working with them to determine how much of this bias is due to TCCON and how much to OCO-2 (most significant cases seem to be sites near ocean)
Still, we want to have a bias correction of our own in place ASAP
Plots from Steffen Mauceri, JPL
GGG2020
GGG2020 with AICF slope removed

## Slide 9: Temperature- or H2O- based biased correction for XN2O and XCH4 (GGG2020.2)
Comparison of XN2O with surface measurements provides compelling evidence of a temperature-or H2O- dependent error
Likewise, analysis of the XCH4 ADCFs suggests such errors in the 5938 and 6076 cm-1 windows.
Plan to optimize the linelists based on these metrics, then develop a bias correction from retrievals with the improved spectroscopy
XN2O
XCH4

## Slide 10: CO2 & CO (TARDISS) and CH4 partial columns (GGG2020.2)
We now have several algorithms to constrain partial columns from TCCON data
These will initially be done as separate algorithms run at Caltech, then incorporated into GGG post processing
TARDISS upper & lower XCO2
Gas | Sub columns | Method | Applies to
CH4 | Trop vs. strat | HF/N2O correlation | All sites
CO2 | PBL vs. remainder or PBL vs. free trop. vs. strat | TARDISS | All sites
CO | PBL vs. remainder | TARDISS | InSb-equipped sites

## Slide 11: Improved post-processing mechanics (GGG2020.2)
There are some miscellaneous changes planned for the post-processing code
I can handle this…
Oh no…
OH NO…!
Modified from No Boilerplate: https://youtu.be/2hXNd6x9sZs?t=491
Improved multi-detector support
InGaAs
InGaAs
Si
InGaAs
InSb
NetCDF writer cleanup
Maintainability first, speed second
Transition from Python to Rust as second language
?
Notes: Improved multi-detector support
Plan to add a mechanism to keep retrievals from InGaAs, Si, and InSb detectors separate during average_results
Workarounds exist currently via renaming windows, this needs standardized into the post-processing workflow
NetCDF writer cleanup
Incorporating the netCDF writer directly into post processing was a significant change that had to handle lots of complicated edge cases.
Now that those edge cases are known, this is ready to be refactored to improve long-term maintainability as well as error reporting to the user
Improving the speed will be explored, but is secondary to maintainability.
Transition from Python to Rust as second language
Python was a natural choice for the netCDF writer given its wide use in our community
However, it lacks strong compile-time guarantees (even with type hinting)
Managing Python environments also requires some tricky scripting to do automatically
Rust provides very strong compile-time guarantees and manages environments more cleanly
This trades longer development time for better maintainability
There is currently some drama with the Rust leadership. Will wait to see how that resolves before committing to this change.

## Slide 12: Non-linearity correction in I2S (GGG202X)
Thank you to Pauli and Rigel for making the nonlinearity fitting code available to the network.
  Helping us modify this to work with InGaAs-only data (currently needs InGaAs + Si, haven’t tested with InGaAs + InSb)
  Making this easier to use end-to-end is an important task
Since nonlinearity is more common in our data than we expected, incorporating the ability to correct this into I2S will be critical
The current method of hard-coding the correction into I2S is inconvenient, the intention is to make this a parameter in the I2S input file
  If there is enough interest, we could potentially release an I2S2020 version with this functionality added
  We would need some volunteers to test and confirm that such a version introduces no other changes in the spectra produced

## Slide 13: Modeling non-ideal ILS in GFIT (GGG202X)
Implementing variable ILSes in GFIT has been desired for some time.
This would allow the retrieval to better account for instrument errors, e.g. shear/angular misalignment
The current plan is to fit an ILS via an external program (e.g. LINEFIT) and feed that into GFIT via either the runlog or a new input file
  Input via the runlog with parameters OPD, FOVI, AMAL, and a new “shear” parameter would be ideal for traceability, since these values can be stored in the .private.nc files
  There remain technical details to work out in calculating these parameters from LINEFIT modulation efficiencies (MEs)
  Testing will also be needed to quantify how well the runlog parameters capture the information contained in the LINEFIT ME output.
Plots from Geoff & Debra’s 2009 talk. Left = Darwin, above = Lamont.
https://tccon-wiki.caltech.edu/pub/Main/PresentationsandPostersGarmisch/Impact%20of%20Misalignment%20on%20ILS.pdf
See Geoff’s talk for details
Notes: Some examples on https://tccon-wiki.caltech.edu/Main/GfitTreatmentofInstrumentLineShape, but not bad ones

## Slide 14: Improved spectroscopy for N2O, CH4, and CO2 (GGG202X)
As mentioned in the “Temperature-based bias correction” task for GGG2020.2, we believe there are errors in the temperature-dependent broadening of N2O and CH4 lines.
There is also some possible temperature in CO2 windows; one candidate wCO2 window was removed from GGG2020 because of this.
The improvements we find in the spectroscopy from the GGG2020.2 bias correction will be incorporated into GGG202X.
6500 cm-1 window not used in GGG2020

## Slide 15: Support for modern gfortran compilers (GGG202X)
For GGG202X, our development compiler will be at least gfortran v8.5.0
We recognize that gfortran versions 10 and higher do not allow GGG2020 to compile successfully
  Given long development times, we won’t be able to target the latest gfortran compiler at time of release
  However, we will aim to get compilation at least working on gfortran 10/11/12, even if that is not the recommended compiler.
We have not yet isolated the NaN bug in non-Voigt windows on gfortran versions 7 to 9
  We’re not able to reproduce this bug on our system even using v8.5
  This suggests that it is either a machine-dependent problem with e.g. file access or a combination of that and the compiler version
  To really track this down, we need assistance from someone who has encountered this problem

## Slide 16
Using machine learning to extract diurnal cycles from temporally sparse data

## Slide 17: Introduction
Deriving XCO2 Diurnal Cycles from Space Based Column Measurements
XCO2 Diurnal Cycles
XCO2 diurnal cycles give information on regional CO2 drawdown from photosynthesis
Diurnal cycles captured by TCCON reveal an afternoon drawdown in XCO2 from increased photosynthetic activity
XCO2 drawdown can be used to calculate Net Ecosystem Exchange (NEE)
G. Keppel-Aleks et al. Biogeosciences, 2012. doi: 10.5194/bg-9-875-2012

## Slide 18: Methods
Deriving XCO2 Diurnal Cycles from Space Based Column Measurements
Machine Learning Model
Random Forest Model
Features:
Source | Variable
TCCON | XCO2, Solar Zenith, Azimuth, Temperature Delta XCO2, Delta Solar Zenith
GOME/ SCIAMACHY | SIF (monthly averaged)
Subsampled TCCON observations at a mimicked GeoCARB scanning pattern
  3 observations 3.5 hours apart, with randomized start time
What should our models target variable be?

## Slide 19: Methods
Deriving XCO2 Diurnal Cycles from Space Based Column Measurements
Empirical Orthogonal Functions (EOFs)
EOFs are a way of capturing patterns of variability in a data set, with each sequential EOF representing finer variation
For our data, we want to capture 95% variance, which takes 12 EOFs
Model output is the EOF principal components

## Slide 20: Results
Deriving XCO2 Diurnal Cycles from Space Based Column Measurements
XCO2 Drawdown/ Net Ecosystem Exchange
From Diurnal Cycles we can calculate XCO2 drawdown
  Defined as the 6 hour difference in XCO2 centered around solar noon
  Better representation of our model’s accuracy
From drawdown, we can calculate net ecosystem exchange
R2: 0.83
R2: 0.67

## Slide 21
To access additional layout options, on the Home tab, click the down arrow next to New Slide on the menu bar.
To obtain the appropriate marking and handling instructions for your information, visit the Marking and Handling Wizard at https://mh.jpl.nasa.gov and answer a few questions about the information's content. The Wizard complies with JPL’s Prime Contract requirements, and by implementing the marking and handling instructions provided by the Wizard, the document will be in compliance with JPL’s Marking and Handling requirements.
When you find your correct marking, copy it to your clipboard; then on the Insert tab, click Header & Footer, and paste it in the Footer box.