## Slide 1
EM27/SUN observations in the Atacama desert
Matthias Max Frey1, Isamu Morino1, Hirofumi Ohyama1, Takashi Miyata2, Yuzuru Yoshii2

## Slide 2: Outline
Atacama geographical information
Tokyo Atacama Observatory (TAO)
Atacama desert campaign 2023

## Slide 3: Chile, Atacama desert

## Slide 4: Atacama desert topography and reflectance
Mt. Chajnantor
San Pedro de Atacama
~60 km
~90 km
Atacama Desert/Plateau south of San Pedro de Atacama (~90 km x ~60 km)
SRTM15+
ADAM Surface Reflectance Database v4.0
Albedo of Atacama Desert in Jan: 0.25-0.35

## Slide 5: University of Tokyo Atacama Observatory (TAO)
Observatory at Mount Chajnantor at a height of 5640 m
Main purpose: Astronomical observatory (Optical-infrared telescope)
Base facility at San Pedro de Atacama (2400 m)
Additional oxygen supply mandatory at TAO

## Slide 6: EM27/SUN observations January 2023
EM27/SUN observations at highest altitude ever performed (~0.5 atm)
Flawless performance of the instrument
Only 2 – 3 hours of observations on the mountaintop due to safety regulations
Additional observations at the base facility in San Pedro de Atacama in the afternoon

## Slide 7: Preliminary analysis
Results look sensible!

## Slide 8: Preliminary Xluft/Xair analysis
Results look sensible!
However, Xluft/Xair deviates from nominal by 0.5 – 1 % (both PROFFAST2.2 and GGG2020)
Possible reason: GEOS mod files doesn’t extend to the surface for San Pedro de Atacama (lowest layer ends at appr. 3000 m, surface is at 2400 m)
Alternative mod files created using NCEP reanalysis data
Changes more pronounced and systematic for GGG2020, for PROFFAST2.2 more variable

## Slide 9: Preliminary Xluft/Xair analysis
PROFFAST2.2
GGG2020

## Slide 10: Coincident OCO-3 target mode
TAO
SAN PEDRO
OCO-3 overpass January 22 (January 18, less valid data)
XCO2 at the plateau 416.4 ppm (416.2 ppm)
EM27/SUN observations January 21 (at San Pedro de Atacama) and 23 (at TAO), but XCO2 values at overpass time (415.9 ppm) and diurnal variability very similar on both days
For January 18, EM27/SUN XCO2 415.8 ppm