## Slide 1
Anthropogenic CO2 emission estimates in the Tokyo Metropolitan Area
Matthias Max Frey, Hirofumi Ohyama, Isamu Morino, Kei Shiomi, Masahide Nishihashi, Tatsuya Miyauchi, Hiroko Yamada, Makoto Saito, Masanobu Wakasa, Thomas Blumenstock, Frank Hase

## Slide 2: Outline
Measurement campaign overview
Modeling setup
Campaign results
Outlook

## Slide 3: Measurement campaign overview
Campaign period: February – April 2016
  The COCCON Tsukuba instrument arrived March 2016
Objective: Estimate megacity (Tokyo) GHG emissions
Collaboration partners
  KIT
  JAXA
  NIES
  Additional support
    Saitama University
    Sodegaura city government
Ohyama and Frey et al., ACPD, 2023

## Slide 4: Modeling setup

## Slide 5: Lagrangian transport model
Meteorological fields from the WRF model
Horizontal resolution 1 km
Different PBL schemes tested w. r. t. AMeDAS observations
WRF drives STILT model
STILT calculates back trajectories from a receptor location, so called footprints
  1 km spatial resolution
  15 min temporal resolution
Footprints are multiplied with anthropogenic and biogenic fluxes to derive spatially resolved contributions of the emission sources
XCO2 enhancement (ΔXCO2) at each observation site is sum of contributions over all cells

## Slide 6: Anthropogenic CO2 fluxes
Open-Source Data Inventory for Anthropogenic CO2 (ODIAC)
  Global high-resolution (1 km) monthly fossil fuel CO2 emissions database
Large point source (LPS) emission strengths and positions corrected
  Replace grid cells above threshold (>104 tons of carbon per month) with averaged value of neighboring cells
  Add LPS emissions according to Ministry of Environment information
For the corrected inventory, LPS account for 37 % of total emissions

## Slide 7: Additional model settings
Biogenic CO2 fluxes: VISITc model downscaled to 1 km resolution using green vegetation fraction data from the VIIRS sensor onboard the Suomi NPP satellite
Background CO2 concentrations from Tsukuba observations
Estimation of a posteriori CO2 emissions utilizing a Bayesian inversion framework
  Scaling factor for large point source emissions
  3 km spatial resolution for nonpoint source emissions
  Biogenic fluxes not optimized

## Slide 8: Results

## Slide 9: XCO2 and XCH4 measurement timeseries
XCO2 (XCH4) daily maxima show large variability with peaks up to 415 ppm (1.87 ppm)
XCO2 daily minima 403 – 405 ppm
XCH4 daily minima show large variability 1.82 – 1.85 ppm due to synoptic-scale events

## Slide 10: Diurnal XCO2 differences
XCO2Diff defined as XCO2 differences from daily background values common to the three sites (5th percentile of Tsukuba measurements throughout each day)
Average XCO2Diff value per 15-min bin calculated for each site using the entire campaign dataset is shown below
Higher variability and XCO2Diff for urban sites
For Tsukuba XCO2Diff decreases during the day due to moderate effect of photosynthesis

## Slide 11: XCO2 simulations
XCO2 enhancements at the three sites
Non-point source contributions dominate ΔXCO2 in Saitama and Tsukuba
LPS and non-LPS ΔXCO2 contributions are comparable in Sodegaura
For model-observation comparison, background XCO2 values must be added to the simulated ΔXCO2, calculated as the difference between observed Tsukuba XCO2 values and simulated Tsukuba ΔXCO2 values

## Slide 12: Observation and simulation comparison
Simulations were performed on days with over 2 h of observations and when the 15-min pooled data showed enhancements of at least 1 ppm between urban and rural site two or more times
Generally good agreement
Inversion significantly improves the comparison
XCO2 timeseries at Saitama and Sodegaura
Example days

## Slide 13: Emission estimation
Optimized spatial emission pattern still largely resembles the prior emissions
Spatial readjustments in part agree with national bottom-up emission inventory MOSAIC
Absolute difference between prior and posterior emissions 1 % (LPS -14 %, Non-LPS 10 %)
Inversion analysis reduced the uncertainty in the total emissions by a factor of ~2
Inversion optimized emissions 277.8 Mt CO2 / y for Tokyo metropolitan area
Good agreement with administrative emission report (250.6 Mt CO2 / y )

## Slide 14: Summary and outlook
We conducted a measurement campaign in the Tokyo Metropolitan area February – April 2016
We developed an urban-scale inversion system to estimate CO2 emissions at >3 km spatial resolution
Our EM27/SUN measurements can properly constrain CO2 emissions in this urban setting
Future tasks:
  Operational megacity observation for more frequent emission estimates
  Investigation of methane emissions
  Integration of satellite data (GOSAT-GW, OCO-3)

## Slide 15: Thank you for your attention!

## Slide 16: Tokyo-Seoul campaign #1, 14-25 Feb 2022
Collaboration: NIES (Frey, Morino, Ohyama, Müller, Tanimoto), Seoul National Univ. (Sujong Jeong, Hayoung Park)
Objective: Monitoring changes of CO2, CO, CH4 in the urban atmosphere on different scales: now and in future; Test for the long-term validation of GOSAT-GW in central Tokyo and Seoul
XCO2
XCO
XCH4
XCO2 [ppm]
ΔXCO2 [ppm]
Timeseries of the EM27/SUN measurements in Kanto at the three stations Tsukuba, Tokyo, and Yokosuka
Comparison of observation and modelling results on February 16