## Slide 1
Band Parameters
SFIT Retrieval Workshop
J Hannigan
NCAR, Boulder, CO November 2019

## Slide 2: Outline
Review of band parameters
Review of spectra parameters
Summary

## Slide 3: Band Parameters 1/6
    The Band Parameter section defines the regions to be fitted.
    There can be several bands. They are numbered 1, 2, … and should be numbered in increasing wavenumber order.
    The current value of MAXBND=125 (huh?!) set in params.f90
    Bandpass limits are used to determine range of lines stored by hbin
    Bandpass limits are used to create the spectra in the t15asc file

## Slide 4: Band Parameters 2/6
    # Microwindows and their parameters from CO2 isotope example
    band = 1
    band.1.nu_start = 4872.000
    band.1.nu_stop = 4888.000
    band.1.calc_point_space = 0.900E-03
    band.1.wave_factor = 1.000
    band.1.max_opd = 100.000
    band.1.omega = 1.914
    band.1.apodization_code = 0
    band.1.snr = 800.0
    band.1.zshift = T
    band.1.zshift.type = 1
    band.1.zshift.apriori = 0.000
    band.1.zshift.sigma = 0.0100
    band.1.beam = 1
    band.1.beam.model = IP
    band.1.beam.1.apriori = 0.01161 1.97530 4882.98981 0.00000
    band.1.beam.1.sa = 0.01 0.01 0.01 0.000
    band.1.gasb = CO2 O13CO CO18O HDO H2O H218O
    band.1.tempretb = F

## Slide 5: Band Parameters 3/6
    calc_point_space – DN – a desired spacing that the forward model will use for the monochromatic spectrum. Actual spacing will be the nearest value to this that is an integer multiple of the observed spectrum spacing in the t15asc file. All spectra in this band must have the same spacing. Keep track of NSPAC.
    wave_factor – WAVFAC – a scaling that can be applied to the spectra wavenumber values. (I never used this)
    max_opd – PMAX – optical path difference of this spectrum [cm]
    omega - OMEGA – aperture diameter / focal length [rad]
    apodization_code – IAP – defined in BOBAPD
    snr – SCNSNR – an snr for all spectra in this band, is overridden by value in t15asc (hence a default value)
    # Microwindows and their parameters from CO2 isotope example
    band = 1
    band.1.nu_start = 4872.000
    band.1.nu_stop = 4888.000
    band.1.calc_point_space = 0.900E-03
    band.1.wave_factor = 1.000
    band.1.max_opd = 100.000
    band.1.omega = 1.914
    band.1.apodization_code = 0
    band.1.snr = 800.0
Apodization Codes: 0 – Boxcar 1 -3 Norton Beer (weak, med., strng) 4 - Denver data 5 – Triangle 6 - Happ – Genzel 7 – KPNO Atmospheric Spectra A 8 – KPNO Atmospheric Spectra B 9 – Hamming function

## Slide 6: Band Parameters 4/6
    # Microwindows and their parameters from CO2 isotope example
    band.1.zshift = T
    band.1.zshift.type = 1
    band.1.zshift.apriori = 0.000
    band.1.zshift.sigma = 0.0100
    band.1.gasb = CO2 O13CO CO18O HDO H2O H218O
    band.1.tempretb = F
    zshift – F_ZSHIFT – flag to switch on a zero shift in this band
    zshift.type - IZERO – function code – see right ->
    zshift.apriori - ZSHIFT – initial zero shift
    zshift.sigma - SZERO – zero shift uncertainty required when retrieving
    gasb - GASB – list of gases to retrieve in this band
    tempretb - TRETB – flag to retrieve temperature using this band
IZERO Codes: 0 – zero shift the spectrum using the a priori value as given – do not fit 1 - retrieve zero level for this band 2 - use zero level from first band in list for this band
Important distinction between an absorption feature in a given bandpass and retrieving it. In short, if a gas is in the GASB list, then there is a block the K matrix for that gas / wavenumber remember K = ∂F/∂x. F is the forward model ie. spectrum and, x is the state vector. GASB is used to build the K matrix.

## Slide 7: Band Parameters 5/6
    # Microwindows and their parameters from CO2 isotope example
    band.1.beam = 1
    band.1.beam.model = PS
    band.1.beam.1.apriori = 0.01161 1.97530 4882.98981 0.00000
    band.1.beam.1.sa = 0.01 0.01 0.01 0.000
    beam - NBEAMS - number of beams in this bandpass, (MAX_NUM_OF_BEAMS = 20 – way too many)
    model - CHANNEL_MODEL_OF_BAND - model for implementation of a realized channel spectrum
              PS: phase shifted reflecting model or
              IP: interferogram perturbation model
    apriori - CCIPARM - parameters used:
              Amplitude of channel [fractional value]
              Frequency [cm-1]
              Wavenumber of zero amplitude [cm-1]
              Linear scale to a change in amplitude [fractional/wavenumber]
    sa - SCHAN_SCALE - uncertainty of each parameter – if value is zero it will not be fit.

## Slide 8: Band Parameters 6/6
    Note on NSPAC
    Ratio between the spacing of the observed spectrum and monochromatic spectrum
    A cross-section value is calculated at each monochromatic point / layer / gas. So it s computationally expensive to have NSPAC large.
    For high resolution work where point spacing is already very small a value of 3-4 seems to work well.
      Note smaller spacing reduces interpolations during the wavenumber shifts
    For lower resolution e.g. 1 cm-1, a much higher value seems to work better, why?

## Slide 9: Spectrum Parameters 1/2
    # spectrum parameters
    sp.snr = 1 2
    sp.snr.1.nu_start = 4882.0
    sp.snr.1.nu_stop = 4888.0
    sp.snr.1.snr = 200.0
    sp.snr.2.nu_start = 4884.3
    sp.snr.2.nu_stop = 4884.5
    sp.snr.2.snr = 0.01
    snr - NSNR – List of number of snr ranges (MAXSNR = 20)
    nu_start - WWV0 – Low wavenumber for this snr range
    nu_stop - WWV1 – High wavenumber for this snr range
    Snr - GSTNR – Constant SNR for this range
    This functionality was first implemented to de-value a section of a spectrum in the fit. For instance a feature that is has a bad line parameter can have a low SNR (=0.01 ?) set and its poor fit will largely have no effect on the retrieval.
    It can be used to override the SNR in the t15asc file

## Slide 10
Note on SNR
In the OE method the statistics Sa on the state vector x and Se on the measurement y are of ultimate importance. After the SNR for each point in the observed spectra is defined per rules listed above Se = 1/SNR. But the Gaussian noise on an FTIR spectrum constant and can be measured. Hence be very aware that any change will manipulate the retrieval.
Spectrum Parameters 2/2

## Slide 11: Summary
The band parameters provide a lot of flexibility to tailor your retrieval.
Some parameters are still there but may not serve a contemporary use in one’s view but may still have utility for some users.
As with all parameters it’s the users responsibility to know what to use and what affect a default value is having.
Its important to know how the Sa values ‘mix’ in the retrieval.

## Slide 12
end