## Slide 1: Volkamer Group Research

## Slide 2: Solar Occultation Flux (SOF)
Kille et al., 2017, AMT
Species | Interfering species | Wavenumber range
NH3 | O3, H2O, CO2, C2H4 | 950 – 980 cm-1
CO | H2O, CH4 | 4270 – 4303 cm-1
C2H6 | CH4, H2O, O3, C2H4, H2CO, HCl | 2970 – 3000 cm-1
C2H4 | H2O, NH3, O3, CO2 | 940 – 1000 cm-1
CH3OH | CO2, O3, H2O, NH3 | 980 – 1040 cm-1
HCOOH | O3, H2O, NH3, CO2, CH4 | 1090 – 1120 cm-1
… |  | 
Digital solar tracker coupled to a Fourier transform infrared spectrometer (FTIR)
  Using EM27 (0.5 cm-1 resolution), 2 second spectra
ZnSe window
Notes: No inlets
Columns average over inhomogeneity within a plume

## Slide 3: Quantifying fluxes in the field
Wind
Measure concentration, wind speed and direction Calculate flux
Column measurement integrates over vertical inhomogeneities
Fly under the plume and measure the changes in the solar spectrum in and out of plumes

## Slide 4
CU SOF
Zenith Sky DOAS (ZS-DOAS) - CU
In situ aerosol sizer/counter
DOAS and SOF to measure columns/quantify fluxes
Lidar to measure plume heights
In situ aerosol and trace gas (O3, CO2, CO), wind sensors for in plume measurements
Direct Sun DOAS (DS-DOAS) - CU
2018 BB-FLUX payload
Wyoming Cloud Lidar

## Slide 5: BB-FLUX- July to September 2018
37 RFs to 18 fires (60+ profiles & 125+ plume underpasses)
Mendocino
Stone
Hirz
Sheep Creek
South Sugarloaf
Watson Creek
Tepee
Miriam
Terwilliger
Pole Creek/
Bald Mountain
Stewart Creek
Rabbit Foot
Sharps
Reynolds Lake
Rattlesnake Creek
Mesa
Keithly
Notes: Mention that did multiple passes for each RF to probe temporal variability during one day
Did repeats to probe variability over multiple days
Transition to next slide using the equation

## Slide 6: V Group SFit
Running on Windows 10 using Windows Subsystem for Linux (instructions available)
Using Python 2.7, will test 3 shortly
Igor runs batch files to call Python to call SFit