## Slide 1
Melanie Follette-Cook (Morgan State University/NASA GSFC), K. Pickering (U. of Maryland), J. Crawford (NASA LARC), W. Appel (EPA), G. Diskin (NASA LARC), A. Fried (U. of Colorado), C. Loughner (ESSIC/NOAA ARL), G. Pfister (NCAR),
A. Weinheimer (NCAR)
DISCOVER-AQ Science Team Meeting
May 3, 2017
Frequency of spatial and temporal gradients during DISCOVER-AQ:
Relevance to geostationary observations of air quality

## Slide 2: Motivation
The Tropospheric Emissions: Monitoring of Pollution (TEMPO) instrument will be the first NASA mission to make atmospheric composition observations from geostationary orbit
We want to quantify the variability that a geostationary instrument like TEMPO would observe.
Is the resolvable variability sufficient to answer the relevant science questions for this proposed geostationary instrument?

## Slide 3: DISCOVER-AQ observations and simulations
Maryland
WRF/Chem - 4km
Follette-Cook et al. 2015
Texas
WRF/CMAQ - 4km
C. Loughner
California
WRF/CMAQ - 4km
W. Appel
Colorado
WRF/Chem - 3km
G. Pfister

## Slide 4: Structure Functions
< > = the average of data pairs separated by distance or time y
Z = variable of interest at given location x
q = scaling exponent (here q =1)
(Z, y)<Z(x + y) - Z(x)q>
We calculated structure functions for in-situ aircraft observations taken during each of the four DISCOVER-AQ campaigns, as well as for collocated simulation output
Though the structure function yields a mean by definition, we analyze the distributions of the trace gas differences at several separation distances

## Slide 5: Do the simulations reproduce the observed variability?
25th 50th 75th 85th 95th Mean
O3
CA
MD
TX
Simulation – Obs (ppbv)
CO
Distance (km)
Time (hr)
MD
CA
TX
CO
These plots show the (simulated-observed) difference between corresponding percentiles of the simulated and observed distributions calculated using the structure function equation
Spatial
P-3B Aircraft (0 – 2 km)
Temporal
Surface observations

## Slide 6: Do the simulations reproduce the observed variability?
NO2
Simulation – Obs (ppbv)
Distance (km)
CA
MD
TX
CO
25th 50th 75th 85th 95th Mean
Spatial: Models overestimate the spatial variability in NO2 in MD and CO, and underestimate in TX.
Temporal: In absence of continuous true-NO2 surface obs, we examine the simulated diurnal variability of NO2. Diurnal changes appear to be well captured by the models.
MD
CA
CO
TX
Hour (local time)
NO2 (ppbv)
P-3B Model
Spatial
Temporal

## Slide 7
Do the simulations reproduce the observed variability?
HCHO
25th 50th 75th 85th 95th Mean
P-3B Model
Spatial
Temporal
HCHO (ppbv)
Hour (local time)
MD
CA
CO
TX
Simulation – Obs (ppbv)
Distance (km)
MD
CA
CO
TX
Spatial: All models underestimate HCHO variability during each campaign
(~ < 2 ppbv)
Temporal: All models capture observed diurnal variability in HCHO. MD simulation shows an underestimation in HCHO in the afternoon

## Slide 8: Frequency of observable gradients
Precision Requirements (PR) for TEMPO
TEMPO spatial resolution: 8 x 4.5 km2
* calculated quantity
** Lok Lamsal, personal communication
Species | Altitude range | STM Precision |  | Temporal Revisit
O3 | 0-2 km | 10 ppbv | 1.7 DU* | 2 hr
O3 | Tropospheric column | 10 ppbv | 6.2 DU* | 1 hr
NO2 | Tropospheric column | 1x1015 molec/cm2 | 1 ppbv** | 1 hr
HCHO | Tropospheric column | 1x1016 molec/cm2 |  | 3 hr
How often and over what spatial and temporal scales were simulated point to point differences larger than the TEMPO precision requirements?

## Slide 9: Frequency of observable spatial gradients
O3
Maryland
Urban-to-suburban scales (12-24 km) show percentages that are likely associated with air quality events (20-40%). On urban-to-rural (40+ km) scales, percentages increase to roughly 60% of the time
Spatial gradients largest in the afternoon (after 2 pm LT) (not shown)
Baltimore

## Slide 10: Frequency of observable spatial gradients
O3
TX and CO show less spatial variability than MD
Lower percentages are likely due to the relatively few air quality events observed during the two campaigns
Texas
Houston
Colorado
Ft. Collins
Denver

## Slide 11: Frequency of observable temporal gradients
O3
Temporal differences in O3 are largest 6 h apart, consistent with the production of O3 throughout the day
Maryland
Colorado
Texas

## Slide 12: Frequency of observable spatial gradients
NO2
Spatial gradients over urban areas are larger than the TEMPO PR
>90% of the time
Overall, NO2 variability appears to be well captured by the proposed precision requirement
Maryland
Texas
California
Colorado
Fresno
Visalia
Bakersfield

## Slide 13: Frequency of observable temporal gradients
NO2
Maryland
Texas
California
Colorado

## Slide 14: Frequency of observable spatial and temporal gradients
HCHO
Maryland – Spatial
Maryland – Temporal
Maryland
Texas
4 days
5 days
6 days
HCHO 1 day
2 days
3 days
4 days
5 days
6 days
HCHO 1 day
2 days
3 days

## Slide 15: Conclusions
O3 (0–2 km):
  In MD, spatial gradients were detectable ~60% of the time for urban-to-rural scales and 20-40% of the time for urban-to-suburban
  Spatial gradients in TX and CO were not as large, but both campaigns had fewer AQ events
  Temporal differences in O3 were largest 6 h apart, consistent with the production of O3 throughout the day
NO2 (tropospheric column):
  Spatial gradients in NO2 were visible > 90% of the time for substantial portions of each region
  One-hour temporal differences in NO2 were detectable at least 50% of the time, increasing to at least 90% for 4-5 hour differences
  Overall, NO2 variability appears to be well captured by the proposed precision requirement
HCHO (tropospheric column):
  All percentages were <10% for all distances and times for the CA, TX, and CO campaigns
  Each model simulation underestimated the spatial variability in HCHO, so these results should be considered a minimum with respect to observable spatial gradients in HCHO

## Slide 16: Thank you!