## Slide 1
Summer ozone in the Northern Front Range Metropolitan Area - Results from a ‘Weekend-Weekday’ analysis
FRAPPE Science Team Meeting May 2017
Andrew Abeleira
Delphine Farmer
Colorado State University
Chemistry Department
Abeleira, A. A. and Farmer, D. K.: Summer ozone in the Northern Front Range Metropolitan Area: Weekend-weekday effects, temperature dependences and the impact of drought, Atmos. Chem. Phys. Discuss. in press, 2017
Funding: Grant NA14OAR4310148
Data: EPA/CDPHE
Notes: -I will be presenting work regarding the Weekend-Weekday effect in the Front range utilizing EPA and CDPHE ozone and NO2 monitors, with funding from NOAA.
-I’d like to acknowledge the Farmer Group and my adviser Delphine Farmer, and also the FRAPPE science teams and organizers.

## Slide 2
Why is O3 increasing or stagnant in the NFRMA with decreasing NO2?
Notes: The question that we are interested in is why is O3 increasing or stagnant at sites across with the Front Range even though NO2 has been decreasing?
-Here are the sites in the Front Range that I have focused on.
-When I initially began this investigation I was focused on generating a spatially diverse analysis, and thus left out some of the other Denver sites since there are quite a few, and I focused on the ones with NO2 data also, but I do have results from the ther Denver sites as extra slides.
-In the Denver area we have two monitoring sites with long term NO2 and Ozone measurements (CAMP and Welby). The CAMP site definitely has a higher traffic density as it is right in downtown Denver, near the interstate and the stadium, which Welby is slightly north east and abuts the Rocky Mountain Arsenal open space. Other sites of interest are the Rocky Flats site adjacent to the Rocky Flats wildlife refugee outside boulder, and then the Fort Collins and Greeley metro sites.

## Slide 3
Why is O3 increasing or stagnant in the NFRMA with decreasing NO2?
Ozone
NO2
2000 - 2015
2000 - 2015
2000 - 2015
Notes: -Here I am showing box and whisker plots of for ozone and NO2 at monitoring sites in the Front Range for the period of 2000-2015 depending on data availability.
-Data here is for June 1st to August 31st 10:00am – 4:00pm local, with years excluded that have <50% of the summer time frame data.
-We see either potentially increasing or stagnant ozone levels at the 5th to 95th percentiles, while NO2 has been decreasing since at least 2003 in the Denver region.
-We can take simple linear regression of the different percentiles versus years.
-2011 Regional Haze reduction plan aimed at reducing haze in the front range, and includes NOx reductions.
-2014 regulation in Colorado to significantly reduce VOC emissions from ONG sector

## Slide 4
Why is O3 increasing or stagnant in the NFRMA with decreasing NO2?
Ozone
NO2
Notes: -Here I have two figures, on the left are the slopes bounded by the 95% CI of the ozone versus year regression for the 6 ozone sites for the 5th, 50th, and 95th percentiles, and the right is the same for the two NO2 sites.
-At the CAMP and Welby sites we see statistically significant increases in ozone at all percentiles, but statistically significant NO2 decreaseds at the 95th and 50th percentiles for the camp site. The welby site has a 95th percentile decrease that straddles statisfically signicance. The rest of the ozone sites are stagnant.

## Slide 5
‘Weekend-Weekday effect’-
Perturbation experiment to investigate O3 production regimes
Notes: -The Weekend/weekday effect has been well documented at urban, rural, and transitionary monitoring sites around the country since the 1970s.
-This type of analysis typically utilizes differences in day of week human behavior/patterns, specifically differences in traffic patterns.
-Here I am showing an example of that, with ozone and NO2 medians shown as the think central line for black or blue, bounded by the 33rd and 67th percentiles.
-We see a sharp drop off from weekday to weekend NO2, with a concurrent small increase in ozone.
-The increased ozone at sites with decreased NOx is typically attributed to the drop off in light and heavy duty commercial trucking on the weekends which reduces NOx emissions more substantially than VOC emissions thus shifting the VOC/NOx ratio, which affects local ozone production.
-Various observational and modeling studies hyprothesis that this is the major cause of the weekend weekday effect, but some also claim that factors such as differences in timing of precursor emissions can also affect observed ozone.
-What I’m going to focus on are broad observational trends in the weekend/weekday effect and central tendencies of ozone in the area, and what that can tell us about the ozone production regime in the Front Range. I will not be addressing differences in weekend and weekday peak ozone events.

## Slide 6
Site specific traffic patterns vary between weekday and weekend
Notes: -I want to start with looking at timing of NO2 emissions at the two sites with longterm NO2 in Denver.
-Here I present diel NO2 profiles at the CAMP and Welby sites for Wedsnesdays and Sundays at both site.
-NO2 is binned into 2 hour bins from midnight to midnight with lighter shades representing earlier years and darker shades later years in the 2000-2015 period.
-There are substantial differences between measured NO2 between sites for similar days, and between weekdays and weekends at the same site.
-Weekdays at CAMP we see a morning rushhour bump followed by an afternoon dip and second evening rushhour bump. At the welby site only the morning weekday rushhour is evident.
-For both sites on Sundays the morning rushhour is suppressed with no evening rushhour present.
-The shaded regions represent the daytime hours I used into the rest of the analysis.
-I thought I would see some substantially differences in the ozone diel cycles for the same sites, but found that to not really be true.

## Slide 7
‘Weekend-Weekday’ trend of O3: Magnitude of concentration, not timing
Notes: -Same style plots, but with ozone instead of NO2.
-The average diurnal magnitudes for welby are greater than CAMP, likely as a result of more ozone titration at CAMP from fresh NO emissions around the monitoring area, and reducing ozone production due to higher NO2 pushing the area into a more NOx saturated regime than Welby.
-The difference in ozone between Sunday and Wednesday is easily discernable for the CAMP site, but not for Welby.
-The CAMP site appears to have an elongated peak Wednesday peak relative to welby, and possibly relative to Sundays at CAMP, which could be indiciative of continued ozone production later in the day from the injection of fresh NO during the later day rush hour, but I have not investigated that further.

## Slide 8
‘Weekend-Weekday effect’: O3 production in Denver is
NOx-Saturated transitioning to peak production
I-25
Welby
La Casa
CAMP
2007
2012
2015
2015
(a)
(b)
(d)
(c)
Notes: -This figure is a little busy to let me walk you through it.
-Lets start with this box here (a).
-Average daytime ozone is in black, and NO2 in blue for Weds and Suns for 2007 2012 and 2015 at the camp site, and then here for the Welby site. I will talk about the other two sites in a bit.
-If we walk through the CAMP box we see very different NO2 for weekdays and weekends, but those differences seem to be decreasing.
-We see increased ozone on the weekends, but those differences also appear to be decreasing in magnitude.
-While at the Welby site, which is only ~10 miles away, we see small changes if any, between weekdays and weekends. And no significant changes in ozone.
-The I-25 sites have just come on recently with a couple years of data. The I-25 site is what I sounds like, and sits essentially right next to I25 and is bombarded by fresh emissions. We ee that the 2015 NO2 cocentrations are higher than 2007 or 2012 at the CAMP site.
-And the La Casa site demonstates an observable difference in NO2, but not ozone.

## Slide 9
‘Weekday-Weekend effect’: O3 production in Denver is
NOx-Saturated transitioning to peak production
Weekdays
Weekends
Notes: -We can plot those weekday and weekend ozone values against the weekday and weekend NO2 values, and tether them.
-Here I am showing ozone versus NO2, the dashed line is a theroreticl ozone production curve calculated from a simple analytical model, it is here to guide ones eye.
-The tethered ozone and no2 values fall along a curve similar to an ozone production curve.
-This tells us that both the camp and welby sites are likely transitioning to peak ozone production from being NOx-saturated, with welby in the lead.

## Slide 10
Exploring long-term trends with the ‘Weekend-Weekday’ analysis
Notes: -We can also look at long term trends through the weekend-weekday analysis lense.
-I pulled this data from the busy figure in the previous slide to illustrate the following analysis.

## Slide 11
-
-
Exploring long-term trends with the ‘Weekend-Weekday’ analysis
Notes: We can take the difference in Ozone or NO2 for weekdays and weekends and called that delta Ozone or delta NO2

## Slide 12
-
-
Exploring long-term trends with the ‘Weekend-Weekday’ analysis
Notes: -Which we can then plot for a given year, or as I’ll show in a second, multiple years
-Postive delta values for both species is indicative of a NOx-saturated regime.

## Slide 13
Sites except CAMP at peak O3 production or crossing over, magnitude of downtown Denver ΔNO2 reducing with time
Notes: -These figures are time series of delta ozone on top for the six long term ozone sites, and delta no2 on the bottom for CAMP and Welby.
-Lets start with ozone. The solid grey line is the average of the 6 sites with the shading representing +/- the 95% confidence interval.
-What we see is a general downward trend for most sites towards the zero line, except for the CAMP site. Without NO2 at the other locations it is hard to definitively determine where the other sites sit on the ozone production curve, but delta ozone of the other sites tend to be more similar to Welby, which makes sense since those sites are not likely to have NO2 concentrations similar to or greater than the CAMP site.
-Now, the delta NO2 at CAMP is interesting itself since it appears to be converging with the Welby site. I hypothesize that this is due to the reduction of NO2 emissions from light and heavy duty commercial trucking via the implementation of emission control technology on those fleets, thus the impact of the drop off of those trucks on the weekend is less discernible.

## Slide 14
Conclusions
1) Ozone is increasing or stagnant at sites in NFRMA though NO2 has been decreasing in the Denver area
2) Ozone production is transitioning to peak production around Denver, but might have crossed the peak in other areas
4) More NO2 monitors need to be collocated with ozone monitors in the NFRMA
3) If we are moving towards a NOx-limited regime reducing VOCs and NOx simultaneously may be effective for reducing O3, but soon VOC reductions may be less effective if we reach low enough NOx
Abeleira, A. A. and Farmer, D. K.: Summer ozone in the Northern Front Range Metropolitan Area: Weekend-weekday effects, temperature dependences and the impact of drought, Atmos. Chem. Phys. Discuss. in press, 2017