## Slide 1
Front Range Air Pollution and Photochemistry Éxperiment
PIs: Gabriele Pfister and Frank Flocke
National Center for Atmospheric Research (NCAR)
National Center for Atmospheric Research (NCAR), NASA Airborne Science Program
Colorado Department for Health and Environment (CDPHE), Colorado State University (CSU), University of Colorado Boulder, Environmental Protection Agency (EPA) Region 8,
National Oceanic and Atmospheric Administration (NOAA), National Park Service (NPS), Regional Air Quality Council (RAQC), UC Berkeley, UC Irvine, UC Riverside, US Naval Academy, U of Wisconsin, U of Rhode Island, U of Cincinnati, Georgia Tech, GO3 Project, Aerodyne Inc., and others
Funded by State of Colorado & National Science Foundation
Jointly with NASA DISCOVER-AQ
PI: James Crawford
Northern Front Range Metro Area (NFRMA)
July 15 - August 18, 2014
http://www2.acd.ucar.edu/frappe

## Slide 2: FRAPPÉ and DISCOVER-AQ
Merging of two major field campaigns to provide a most comprehensive look at air quality in the Colorado Front Range
Improve development & evaluation of emission control strategies
Allow better modeling of present and future air quality for decision making
Identify optimal locations for surface monitoring sites making the network more efficient and more representative
Refine and verify satellite data for air quality planning in the Front Range.

## Slide 3: FRAPPÉ E&O
Open House (2 August) and Media Day (15 July) at RAF
Outreach oriented webpages
Student and teacher involvement
2-day educator workshop
Videos, flyers, brochures, stickers
Public presentations and displays
Public involvement (AQ hikes, personal exposure monitors, ... )
Media and Press

## Slide 4
Mission Summary and Preliminary Findings
Picture: Samuel Hall (NCAR)
Joint FRAPPÉ and DISCOVER-AQ Science Team Meeting
4-8 May 2015

## Slide 5
MEASUREMENTS
Data Archive
http://www-air.larc.nasa.gov/missions/discover-aq

## Slide 6
Aircraft
NASA P3
15 Flights
NASA B200
16 Flights
NCAR C130
17 Flights (2TF)
NASA Falcon
10 Flights
NASA Aircraft pictures by Paul Filmer, NCAR C130 picture by Sam Hall
FRAPPÉ and
DISCOVER-AQ Flights

## Slide 7
NASA P-3 Flight Tracks - NOx
Repetitive flightpattern

## Slide 8
NCAR/NSF C-130 Flight Tracks - NOx
Targeted, regional flights

## Slide 9
Date | Objective
0726 (RF01) | Front Range emissions
0727 (RF02) | Front Range emissions & Denver Cyclone
0728 (RF03) | Front Range emissions & Denver Cyclone & Transport to NW out of Fort Collins
0729 (RF04) | Large scale pollution over NW Colorado and S WY & Jay’s CAFO & Pawnee PP
0731 (RF05) | Mountain-valley (not well developed)
0802 (RF06) | Mountain-valley
0803 (RF07) | Mountain-valley
0806 (RF08) | Piceance and Uintah Basin & Hayden and Craig PP
0807 (RF09) | Front Range Emissions
0808 (RF10) | P-3 Intercomparison & Platte River valley flow
0811 (RF11) | Mountain-valley
0812 (RF12) | Mountain-valley
0815 (RF13) | Inflow from WY (not found) & Hayden, Craig, Ute PP, Rifle OG & SE outflow
0816 (RF14) | SE Outflow & TES overpass – 2 spirals
0817 (RF15) | Front Range emissions & Piceance Basin emission to Front Range & Upslope
FRAPPÉ Flight Objectives

## Slide 10
Six ground sites at P-3 spiral locations Erie/BAO, Platteville, Fort Collins, Downtown Denver, Chatfield, Golden/NREL In-situ instruments, tethered balloons, LIDARs, ozone sondes, vertical profiles up to 1000 feet.
Ground monitors set up by EPA / CDPHE specifically for the campaign
  In addition to existing ground network
Ozone and VOC sampling on E-W gradient
  Along ~40N, between Erie and the Continental Divide
6 Mobile labs
  Operating from Eastern Plains to Continental Divide
  Sampling of oil and gas facilities, CAFOs, Commerce City, Metro Area & Foothills
Tethered balloons
  Ft Collins, Downtown, Chatfield
Small monitors, PANDORA spectrometers, etc.
Picture by Andy Langford
Ground Measurements

## Slide 11
Surface Monitors

## Slide 12
Surface Monitors
Notes: The orange circles show the major ground sites with more than ozone, Pandora and maybe NOx.

## Slide 13
Mobile Units

## Slide 14
Mobile Units

## Slide 15
Mobile Units

## Slide 16
Mobile Units

## Slide 17
Some First Results
SOURCES
PRELIMINARY Analysis !
Cory Wolff, NCAR/RAF

## Slide 18
O&G: Ethane to Methane Ratio
8% Ethane*
5% Ethane*
*Composition of Natural Gas
as provided by Xcel Energy
Wattenberg (C-130)
Western Slope (C-130)
8% Ethane*
5% Ethane*

## Slide 19
Hannah Halliday, Penn State University
Surface PTRMS & P-3
O&G: Benzene @ Platteville

## Slide 20
Agriculture:
Ammonia as a Tracer
C-130
Downwind of feedlots

## Slide 21
Fingerprinting Methane
Amy Townsend-Small, U Cincinnati
Tracer – tracer correlations (e.g. Methane vs Ammonia and Ethane)
Methane isotope analysis
?
d2H signature ~-202‰
d2H signature ~-290‰
d2H signature ~-290‰
Platteville: d2H signature ~-250‰
-> ~ equal contribution of O&G and agricultural sources

## Slide 22
Hayden
Craig
Bonanza
Valmont
NOx
SO2
Power Plants – C-130 NOx and SO2

## Slide 23
Currently available: NEI 2011 (provided by Stu McKeen), WESTAR (2011, upon request), Other?
Need region specific emissions & speciation & year specific
Update emissions based on observations
Form Front Range emission and modeling working groups (proposed by K. Briggs, CDPHE)
P-3 Benzene (<3km)
WRF-Chem Benzene (<3km)
NEI 2011 Benzene
WRF-Chem Analysis with NEI 2011
For modeling we need better anthropogenic emissions!
 Mean ⏏ Median
P-3
WRF-Chem
Benzene too low, NEI 2011 has mostly urban sources
Data: Wisthaler
Notes: Nox, CO too high
VOCs all over the board

## Slide 24
Evaluations show the model is:
Too high for urban NOx, CO, SO2
Too low for many VOCs, NH3
Off in spatial distribution for some tracers
Incorrect in tracer ratios
Comparison to surface measurements
WRF-Chem Analysis with NEI 2011
Measured
WRF-Chem
WRF-Chem (+50% OG Emis.)
NO, ppb
C2H6, ppb
C3H8, ppb
Acetone, Platteville
PTRMS, Wisthaler
Cans, Helmig
Cans, Helmig
Various

## Slide 25
Some First Results
VOC/Nox Sensitivity
PRELIMINARY Analysis !
Cory Wolff, NCAR/RAF

## Slide 26: NOX sink partitioning
log NOX
Fractional NOX Loss
HNO3
RONO2
Urban
Rural
RH + OH  RO2 + H2O
NO2 + OH  HNO3
RO2 + NO  RONO2
"NOX Oxidation Products and their Relationship to Ozone Production Across Colorado's Front Range"
Tamara Sparks, UC Berkeley
Notes: If look at how ozone produced, NOx and VOC emissions fuel coupled NOx and HOx cycles which spit out ozones.
This cycling ends with termination, including formation of NOx sinks alkyl nitrates and nitric acid
As part of understanding ozone production, I will be focusing on these NOx sinks
  Which NOx sinks are formed depends on these reactions
  If VOC reacts with OH, it produces RO2, then RONO2
  If NO2 reacts with OH, is make HNO3
  So at high NOx, HNO3 dominates
  At low NOx, VOC more likely to react with OH so RONO2 dominates
So if we look back at this picture, we can think of this urban line as where we used to be*

## Slide 27: NOX sink partitioning
log NOX
Fractional NOX Loss
Time
HNO3
RONO2
Urban
Rural
VOCR
RH + OH  RO2 + H2O
NO2 + OH  HNO3
RO2 + NO  RONO2
"NOX Oxidation Products and their Relationship to Ozone Production Across Colorado's Front Range"
Tamara Sparks, UC Berkeley
Notes: But as time goes forward and NOx decreases, urban areas are moving to the left, toward more AN production. But this isn’t a fixed picture that depends only on NOx*
  Alkyl nitrate formation also depends on the VOCs going making the RO2 radicals, so VOC reactivity can shift this picture too

## Slide 28
Fractional NOX Loss
P-3 Aug 3
Mexico City
SOAS
HNO3
RONO2
log NOX
1.5ppb
RH + OH  RO2 + H2O
NO2 + OH  HNO3
RO2 + NO  RONO2
"NOX Oxidation Products and their Relationship to Ozone Production Across Colorado's Front Range"
Tamara Sparks, UC Berkeley
NOX sink partitioning
Notes: So where does this day fall on partitioning plot?
*Right in between, still to right of crossover, but in a region with high gradient where can change quickly with small changes in NOx
This occurs at an average of about 1 ppb
As was mentioned previously, August 3 and July 22 were the ozone exceedance days during the campaign, and I noticed that both of those days had a high fraction of ANs. As I showed before, Aug 3’s calculated production ratio was 32% for ANs, which is among the highest we saw for production. July 22 C130 wasn’t flying, so don’t have a plot of production, but the concentration was 42%, which was the highest of any day based on concentrations. If the greater AN loss from Aug 3 holds on July 22 as well, the production percentage would be even higher, maybe even crossing the 50% mark. So we see a correlation between high ozone and high alkyl nitrate production
Ozone exceedance days had high alkyl nitrates

## Slide 29
Some First Results
Denver Cyclone
PRELIMINARY Analysis !
Cory Wolff, NCAR/RAF

## Slide 30
What the WRF Tracer Model predicted
What the C-130 saw
The “Denver Cyclone”
Notes: DCVZ conditions form when a low-level moist, southeasterly flowing air mass meets the Palmer Divide, a ridge that extends east of the Colorado Front Range. If the moist air lifts over the ridge and meets northwesterly winds originating in the Rocky Mountain foothills, winds may converge to create enhanced cyclonic vorticity.[2]

## Slide 31
Local Emissions - Separation and Mixing
NOx (C-130)

## Slide 32
Ethane (C-130)
Local Emissions - Separation and Mixing

## Slide 33
Ozone (C-130)
Local Emissions - Separation and Mixing

## Slide 34
Some First Results
Residual Layer and Recirculation
PRELIMINARY Analysis !
Cory Wolff, NCAR/RAF

## Slide 35: Case Study: Denver Cyclone Episode of July 26-29
TOPAZ ozone lidar
July 29
July 26-29
High O3 in residual layer
9:39 MDT Aug 8
What is the origin and fate of the high ozone in the nocturnal residual layer?
Polluted layer aloft
8-h O3 of 73 ppbv at Golden on July 28 and 1-h O3 of 84 ppbv at BAO on July 29
Andy Langford, NOAA

## Slide 36
Some First Results
Mountain-Valley Flow
PRELIMINARY Analysis !
Cory Wolff, NCAR/RAF

## Slide 37
Ozone Transport into the Mountains
Evolution of Surface Ozone for 11 & 12 August 2014 Upslope Events
Surface Ozone (ppb)
Day of Year (UTC)
4pm LT
4pm LT
Welby
Denver Downtown
Golden
Mines Peak
Surface Monitoring (CDPHE)
WRF-Chem

## Slide 38
The Figures highlight the transport event for ozone - produced over the Front Range and being pushed westward into the mountains by thermally driven upslope.
This demonstrates how Front Range ozone can impact remote areas up to the divide and into the adjacent valleys on the west side of the divide.
Background
(50 ppb)
Upslope flow
Evening
spillover
C-130
Modeled
12 August 2014
Ozone Transport into the Mountains

## Slide 39
Ozone Transport into the Mountains
12 August 2014
C-130 Ethane
C-130 NOx

## Slide 40
Some First Results
AerosoLS
PRELIMINARY Analysis !
Cory Wolff, NCAR/RAF

## Slide 41
Aerosol composition in Golden was dominated by organics: most of this OA was secondary
Corroborated by AMS measurements on C-130 (Bahreini Group)
Most of the PM was regional (~70%), but a strong local signature was evident most days (~30% of PM) – sources of the local PM (OM, NH4NO3, EC) need to be investigated
Chrisopher Hennigan
University of Maryland
Predominance of organic aerosol species (Average = 75% of fine aerosol mass)
Sunset Labs OCEC Field Analyzer andParticle-into-Liquid Sampler with dual Ion Chromatographs (PILS-IC)
@ Golden Site

## Slide 42
Clearly identified and characterized all emission sources in the Front Range and Western Slopes slope
  Northern Front Range / Greeley / DJ Basin dominated by oil & gas and agricultural emission signatures
  Denver / Boulder urban centers usually dominated by traffic and industrial emissions
Ozone (and secondary organic aerosols) efficiently formed across the region
In the absence of wildfires, this summer’s Front Range air quality was mainly controlled by local emissions.
Air Quality in eastern foothills and to the Continental Divide dominated by Front Range emissions
Elevated regional ozone background
Influence of Western Slope sources on Front Range are small
Transport of front range air pollution into mountains and adjacent valleys was seen regularly.
Outflow from Front Range into Eastern Plains can be significant
Identified potential new / better monitoring locations
Need for improved emission information for AQ modeling
PRELIMINARY Findings

## Slide 43: EXTRAS

## Slide 44
Some First Results
Regional POllution
PRELIMINARY Analysis !
Cory Wolff, NCAR/RAF

## Slide 45
Inflow from the West?

## Slide 46
Regional Ozone Distribution
C-130 All altitudes

## Slide 47
Full chemistry payload on NCAR/NSF C-130
(almost) Full chemistry payload on NASA P3
Roughly equivalent # of measurements at BAO, NREL, Platteville; plus LIDARs
Many important pollutants on six mobile vans
Enhanced CDPHE*( ground network (EPA monitors)
Remote sensing / atmospheric column measurements on two aircraft and at 16 ground locations
Tethered Balloons and Ozone Sondes
Personal Pollution Monitoring
& Comprehensive Modeling Efforts
* Colorado Department of Public Health and the Environment
FRAPPÉ and DISCOVER-AQ Measurement Suite

## Slide 48
C-130 NOx

## Slide 49
C-130 Ethane

## Slide 50
P-3 NOx

## Slide 51
P-3 Ethane

## Slide 52
Benzene Correlations
Canister Benzene correlates better with heavier alkanes, not well with CH4 or ethane
or even propane
C130 Aircraft Benzene also correlates better with heavier alkanes
(TOGA data from 7/28/14 flight)

## Slide 53
Ammonia to Methane Ratio
Color-coded by Ethane

## Slide 54
Ammonia to Methane Ratio
C-130 Flights 12-15 for Front Range

## Slide 55
Valmont
Bonanza
Hayden, Craig
Power Plants – C-130 NOx and SO2

## Slide 56
Typical coal fired
PP plumes
NOx enhancements of 30-45 ppb
converted boilers Cherokee EGU ?
Commerce City – C-130 NOx and So2

## Slide 57
Front Range Outflow (C-130 Ethane)

## Slide 58: All data NASA P3
Benzene
Longitude (deg)
Alt (km)
Platteville
25
0.5
Instead of this one we
could use a slide from Halliday
(see next)

## Slide 59
H. Halliday, Penn State